Parlay 4.0

Parlay X Web Services Specification

Status	:	Public – For Industry Comment

Version	:	1.0

Date	:	9 May 2003

Copyright © The Parlay Group, Inc.. All Rights Reserved. This document and translations of it, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this document itself may not be modified in any way, such as by removing the copyright notice or references to The Parlay Group, except as jointly determined by The Parlay Group and third party. The limited permissions granted above are perpetual and will not be revoked by The Parlay Group or its successors or assigns. This document and the information contained herein is provided on an "AS IS" basis and The Parlay Group DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE." The Parlay Group takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights.

Acknowledgement:

Patent Claims

The Parlay Group received this notification about patent claims from one of the contributors to this specification:

NOTICE: AePONA, Inc. has asserted that it is the holder of International Patent Co-operation Treaty Patent Number PCT/EP01/08854, and that such patent would be infringed upon by the implementation of the Parlay X Specification (the “Specification”) in the absence of an appropriate license. AePONA has agreed to grant a royalty-free, irrevocable, worldwide license to such patent to any party (whether or not a member of The Parlay Group) to the extent necessary to implement the Specification, along with any future versions of the Specification, including any revisions, enhancements, updates, or modifications thereto, consistent with AePONA’s obligations under The Parlay Group Membership Agreement. It is important to note that there may be multiple technical implementations possible for the Specification, some of which may exceed the scope of the license granted. Therefore, any party interested in implementing the portion of the Specification which contains technology covered by the AePONA patent is advised to contact legal@aepona.com.

The Parlay Group takes no position with respect to validity, ownership or potential infringement issues relating to AePONA’s patent or any other legal issues, whether specifically related to the Specification or otherwise. The Parlay Group makes no representations, warranties, or guarantees with regard to whether AePONA or any other party has any intellectual property rights in the Specification that have not been disclosed. All parties interested in implementing the Specification are advised to obtain legal advice related to such implementation, including any intellectual property issues relating thereto.

Co-Copyright and Joint Development with PayCircle

Parlay would like to acknowledge the contributions and joint development work performed between Parlay and PayCircle.  The content of Chapter 7 entitled Payment was a collaborative effort between the two groups.  As a result, both Parlay and PayCircle hold copyrights to Chapter 7.  Please see Chapter 7 for additional details.

Contents

0.1	Revision Control	9

0.2	Specification Status	9

0.3	Contact Information	9

1	Introduction	10

1.1	Purpose of Parlay X	10

1.2	Scope of this Document	10

1.3	References	10

1.4	Definitions and  Abbreviations	10

1.4.1	Definitions	10

1.4.2	Abbreviations	11

1.5	Parlay X Web Services	13

1.5.1	Selection Criteria	13

1.5.2	Implementation Considerations	14

1.6	Optional Parameters	15

1.7	Document Structure	15

2	Common Data Definitions	18

2.1	Record of Changes	18

2.2	Common Data Type Definitions	18

2.2.1	EndUserIdentifier	18

2.2.2	ArrayOfEndUserIdentifier	18

2.2.3	ArrayOfURI	18

2.3	Common Exception Definitions	18

2.4	Common Data Definitions Syntax – WSDL	19

3	Third Party Call	20

3.1	Record of Changes	20

3.2	Overview	20

3.2.1	Description	20

3.2.2	Commercial & Technical Rationale	20

3.2.3	Relationship to Similar or Supplanted Specifications	20

3.2.4	Scenarios	21

3.3	Call API	21

3.3.1	Attempt Immediate Call Set-Up Between Two Addresses	22

3.3.2	Get Current Status of a Call	23

3.3.3	End a Call	23

3.3.4	Cancel a Call Request	24

3.4	Web Service Data Definitions	24

3.4.1	Data Types	24

3.4.2	Exceptions	25

3.5	Web Service Syntax – WSDL	26

4	Network-Initiated Third Party Call	27

4.1	Record of Changes	27

4.2	Overview	27

4.2.1	Description	27

4.2.2	Commercial & Technical Rationale	27

4.2.3	Relationship to Similar or Supplanted Specifications	27

4.2.4	Scenarios	28

4.3	Call API	28

4.3.1	Request Application Handling of a ‘Busy’ Condition	29

4.3.2	Request Application Handling of a ‘Not Reachable’ Condition	30

4.3.3	Request Application Handling of a ‘No Answer’ Condition	31

4.3.4	Request Application Handling of a ‘Called Number’ Condition	32

4.3.5	Request Application Handling of an ‘Off Hook’ Condition	33

4.4	Web Service Data Definitions	33

4.4.1	Data Types	33

4.4.2	Exceptions	34

4.5	Web Service Syntax – WSDL	34

5	SMS	35

5.1	Record of Changes	35

5.2	Overview	35

5.2.1	Description	35

5.2.2	Commercial & Technical Rationale	35

5.2.3	Relationship to Similar or Supplanted Specifications	36

5.2.4	Scenarios	36

5.3	Send SMS API	38

5.3.1	Send an SMS Message	39

5.3.2	Send an SMS Logo	40

5.3.3	Send an SMS Ringtone	41

5.3.4	Get Current Status of an SMS Delivery	43

5.4	SMS Notification API	43

5.4.1	Notify Application of an SMS Message Sent to a Specific Address	44

5.5	Receive SMS API	44

5.5.1	Retrieve All SMS Messages Sent to a Specific Address	45

5.6	Web Service Data Definitions	45

5.6.1	Data Types	45

5.6.2	Exceptions	47

5.7	Web Service Syntax – WSDL	47

6	Multimedia Message	48

6.1	Record of Changes	48

6.2	Overview	48

6.2.1	Description	48

6.2.2	Commercial & Technical Rationale	49

6.2.3	Relationship to Similar or Supplanted Specifications	49

6.2.4	Scenarios	49

6.3	Send Message API	50

6.3.1	Send a Multimedia Message	50

6.3.2	Get Current Status of a Multimedia Message Delivery	52

6.4	Receive Message API	53

6.4.1	Provide Application with Multimedia Messages Sent to the Application	53

6.4.2	Retrieve URI References to the Parts of a Multimedia Message	54

6.4.3	Provide Application with a Multimedia Message as an Attachment	55

6.5	Message Notification API	55

6.5.1	Notify Application of a Multimedia Message Sent to a Specific Address	56

6.6	Web Service Data Definitions	56

6.6.1	Data Types	56

6.6.2	Exceptions	59

6.7	Web Service Syntax – WSDL	59

7	Payment	60

7.1	Record of Changes	61

7.2	Overview	61

7.2.1	Description	61

7.2.2	Commercial & Technical Rationale	61

7.2.3	Relationship to Similar or Supplanted Specifications	61

7.2.4	Scenarios	62

7.3	Amount Charging API	62

7.3.1	Charge Currency Amount to an Account	63

7.3.2	Refund Currency Amount to an Account	63

7.4	Volume Charging API	64

7.4.1	Charge Volume to an Account	64

7.4.2	Convert a Volume to a Currency Amount	65

7.4.3	Refund Volume to an Account	66

7.5	Reserved Amount Charging API	66

7.5.1	Reserve a Currency Amount from an Account	67

7.5.2	Adjust the Currency Amount of an Existing Reservation	68

7.5.3	Charge a Currency Amount against an Existing Reservation	68

7.5.4	Release an Existing Reservation	69

7.6	Reserved Volume Charging API	70

7.6.1	Convert a Volume to a Currency Amount	70

7.6.2	Reserve a Volume from an Account	71

7.6.3	Adjust the Volume of an Existing Reservation	71

7.6.4	Charge a Volume against an Existing Reservation	72

7.6.5	Release an Existing Reservation	73

7.7	Web Service Data Definitions	73

7.7.1	Data Types	73

7.7.2	Exceptions	74

7.8	Web Service Syntax – WSDL	74

8	Account Management	75

8.1	Record of Changes	75

8.2	Overview	75

8.2.1	Description	75

8.2.2	Commercial & Technical Rationale	75

8.2.3	Relationship to Similar or Supplanted Specifications	75

8.2.4	Scenarios	76

8.3	Account Management API	76

8.3.1	Account Balance Query	77

8.3.2	Account Credit Expiration Date Query	77

8.3.3	Account Balance Recharging	78

8.3.4	Account Balance Voucher Recharging	79

8.3.5	Account Transaction History Query	80

8.4	Web Service Data Definitions	81

8.4.1	Data Types	81

8.4.2	Exceptions	82

8.5	Web Service Syntax – WSDL	82

9	User Status	83

9.1	Record of Changes	83

9.2	Overview	83

9.2.1	Description	83

9.2.2	Commercial & Technical Rationale	83

9.2.3	Relationship to Similar or Supplanted Specifications	83

9.2.4	Scenarios	83

9.3	User Status API	84

9.3.1	Get User Status	84

9.4	Web Service Data Definitions	84

9.4.1	Data Types	84

9.4.2	Exceptions	85

9.5	Web Service Syntax – WSDL	85

10	Terminal Location	86

10.1	Record of Changes	86

10.2	Overview	86

10.2.1	Description	86

10.2.2	Commercial & Technical Rationale	86

10.2.3	Relationship to Similar or Supplanted Specifications	86

10.2.4	Scenarios	86

Location enabled Buddy-list:	86

10.3	Terminal Location API	87

10.3.1	Get Location of Terminal	87

10.4	Web Service Data Definitions	88

10.4.1	Data Types	88

10.4.2	Exceptions	88

10.5	Web Service Syntax – WSDL	88

ANNEX A.	Index of Parlay X API Messages	90

Figures

Figure 1: Parlay X Web Services, Parlay X APIs and Parlay APIs	13

Figure 2: Third Party Call Scenario	21

Figure 4: Send SMS Scenario	37

Figure 5: Receive SMS Scenario	38

Figure 6: Multimedia Messaging Scenario	50

## Revision Control

Revisions to this document will be represented by a two part numeric version number. The first part represents a publication (major release) level and the second part represents a revision level associated with the release.  (For example, 0.x represents pre-publication revisions, 1.0 represents the first published release, and 1.x represents post publication revisions of the first release.)

| Issue | Date | Reason for Change |
| --- | --- | --- |
| 1.0 | 9 May 2003 | First Public Release |

The master copy of this document is held in electronic format on the Parlay web site at http://www.parlay.org.

## Specification Status

This document is at version 1.0 and is a part of the Parlay X Working Group documents that contribute to release 4.0 of the Parlay Specifications.

## Contact Information

Contact information for the Parlay Group can be found at http://www.parlay.org.

All product names mentioned within this specification are the trademarks of their respective owners.

# Introduction

## Purpose of Parlay X

The Parlay APIs are designed to enable creation of telephony applications as well as to "telecom-enable" IT applications.  IT developers, who develop and deploy applications outside the traditional telecommunications network space and business model, are viewed as crucial for creating a dramatic whole-market growth in next generation applications, services and networks.

The Parlay X Web Services are intended to stimulate the development of next generation network applications by developers in the IT community who are not necessarily experts in telephony or telecommunications. The selection of Web Services should be driven by commercial utility and not necessarily by technical elegance. The goal is to define a set of powerful yet simple, highly abstracted, imaginative, telecommunications capabilities that developers in the IT community can both quickly comprehend and use to generate new, innovative applications.

## Scope of this Document

This document specifies an initial set of Parlay X Web Services. For each selected Web Service, this document describes the motivation for its inclusion, the commercial and technical rationale, and an illustrative usage scenario(s).  This document also specifies the message(s) exchanged during invocations of each Web Service, by defining the semantics in English and the syntax using W3C WSDL.

## References

The following is a list of references to publicly available supporting documentation.  These documents are of relevance to Parlay X Web Services in general. More specific references, which are applicable to the definition of Common Data or to an individual Parlay X Web Service, can be found in the appropriate section of this document: i.e. from Section 2 onwards.

- Parlay/OSA APIs (Parlay 4.0): http://parlay.org/specs/index.asp

- Parlay X White Paper, Version 1.0: http://parlay.org/specs/library/index.asp

- Parlay Web Services - White Papers, Version 1.0: http://parlay.org/specs/library/index.asp

## Definitions and  Abbreviations

Definitions

(Parlay X) Application

Unless otherwise specified, the document will be using the term (Parlay X) application to refer to software that invokes or can invoke a Parlay X Web Service.

Parlay X Gateway

The term Parlay X Gateway is used to describe the implementation of a set of Parlay X Web Services. In telecommunications parlance an implementation of a Parlay X Web Service on a Parlay X Gateway would also be referred to as a service.

Abbreviations

3GPP	3rd Generation Partnership Project

A/IN	(Advanced) Intelligent Network

AAA	Authorization, Authentication, and Accounting

AM	Account Management

API	Application Programming Interface

APP	Application

CBC	Content Based Charging

CC	Call Control

DIME	Direct Internet Message Encapsulation

EMS	Enhanced Messaging Service

ETSI	European Telecommunications Standards Institute

FW	(OSA/Parlay) Framework

GIF	Graphics Interchange Format

GPRS	General Packet Radio System

IM	Instant Messaging

IP	Internet Protocol

IT	Information Technology

IVR	Interactive Voice Response

JAIN	Integrated Network APIs for the JavaTM platform

JCP	JavaTM Community ProcessSM

JPay	Payment API for the JavaTM platform

MIME	Multipurpose Internet Mail Extensions

MM7	Communication protocol between MMS Relay/Server and MMS Application Server

MMS	Multimedia Message Service

MMS-C	Multimedia Message Service Center

MPS	Mobile Positioning System

MS	Mobile Station

MSC	Mobile Switching Center

MSISDN	Mobile Station ISDN Number

OASIS	Organization for the Advancement of Structured Information Standards

OMA	Open Mobile Alliance

OSA	Open Service Architecture

PIN	Personal Identification Number

PINT	PSTN and Internet inter-networking

PSTN	Public Switched Telephone Network

SAML	Security Assertion Markup Language: i.e. an XML-based security standard for exchanging authentication and authorization information, developed by SSTC)

SCF	Service Capability Feature

SCS	Service Capability Server

SIP	Session Initiation Protocol

SLA	Service Level Agreement

SMS	Short Message Service

SMS-C	Short Message Service Center

SOAP	Simple Object Access Protocol

SSTC	Security Services Technical Committee (of OASIS)

UCP	Universal Computer Protocol

URI	Uniform Resource Identifier

VASP	Virtual Application Service Provider

W3C	World Wide Web Consortium

WAP	Wireless Application Protocol

WG	Working Group

WGS 84	World Geodetic System 1984

WS	Web Service

WSDL	Web Service Definition Language

WS-I	Web Services-Interoperability Organization

XML	Extensible Markup Language

## Parlay X Web Services

Selection Criteria

Each Parlay X Web Service should be abstracted from the set of telecommunications capabilities exposed by the Parlay APIs, but may also expose related capabilities that are not currently supported in the Parlay APIs where there are compelling reasons.  These tiered levels of abstraction, and the Parlay – Parlay X relationship, are illustrated in Figure 1.

Figure 1: Parlay X Web Services, Parlay X APIs and Parlay APIs

The selection criteria for the Parlay X Web Services are as follows:

- The capabilities offered by a Parlay X Web Service may be either homogeneous (e.g. call control only) or heterogeneous (e.g. terminal location and user status).

- The interaction between an application incorporating a Parlay X Web Service and the server implementing the Parlay X Web Service will be done with an XML-based message exchange.  The message exchange should follow the synchronous request/response model and be initiated by the application; the ‘response’ from the Parlay X Web Service is optional.  However asynchronous messages from the Parlay X Web Service implementation (on a Parlay X Gateway) to the application may be defined where there are compelling reasons; e.g. to implement a notification type web service.  In the latter case, the message exchange would invoke an application web service using a similar, synchronous request/response model.

- Parlay X Web Service invocations should not be correlated and the Web Service itself should be stateless from the perspective of the application, unless there are compelling reasons.  In particular, in the case of asynchronous notifications from a Parlay X Web Service implementation (on a Parlay X Gateway) to an application, NO application-initiated invocations to provision (or de-provision) notification-related criteria in the Parlay X Web Service should be implemented.

- Parlay X Web Services follow simple application semantics, allowing the developer to focus on access to the telecom capability using common Web Services programming techniques.

- Parlay X Web Services are not network equipment specific, and not network specific where a capability is relevant to more than one type of network.

- Parlay X Web Services should be based on the reference Web Service technology, as it is defined in the IT world and according to the Parlay Web Services WG recommendations; more specifically, at the moment, WSDL is the chosen standard to invoke and describe Parlay X Web Services.

- The Parlay X APIs should be extendible; integration of third party provided interfaces must be supported using proven, reliable, and standard Web Service technology.

- Parlay X Web Services are application interfaces and do not provide an implementation of AAA (Authorization, Authentication, and Accounting), service level agreements or other environment-specific capabilities. Rather, they shall rely on proven and reliable solutions provided by the Web Services infrastructure.

Implementation Considerations

Versioning

The namespace will contain a version number as a suffix for the service name.  The suffix will be a separate path element consisting of: the letter 'v’ followed by a major version number followed by an underscore and a minor version number.

- The major version number will reflect the version of Parlay X for the last change to the API.

- The minor version number will reflect maintenance of the API between Parlay X versions.

- Example: www.csapi.org/wsdl/parlayx/account_management/v1_0 represents the initial public version of the Parlay X Account Management Web Service.

The rationale for this version number scheme is as follows:

- Prefixing the path element with “v” and using an underscore minimizes the possibility of tool issues.  Using namespace elements that are only digits (or that contain characters other than letters, digits and underscores) may result in issues with different tools - e.g. period is a package delimiter

- Adding the version path element after the API element, instead of after the “parlayx” element, means that as Parlay X changes, that APIs that do not change will not require changes to running services since their namespaces will not change

- Using this convention eliminates parsing and related issues with two digit versions, leading zeros, etc.

- This convention can also be applied to other Parlay X namespaces such as Common Data.

## Optional Parameters

Some parameters are defined as OPTIONAL.  Within a message signature, the XML schema type definition for an optional parameter may use the nillable attribute to allow the actual value of the parameter to be "NULL" (or "NIL").  Since this approach is dependant upon the industry adoption of WS-I's Basic Profile 1.0, which is currently not widely implemented, this version of the Parlay X Web Services specification does not follow this approach.  As a temporary measure this specification explicitly defines “NULL” values for parameters tagged OPTIONAL such that, if used, the actual value of the parameter must be considered "NULL".

The following “NULL” values are defined for each OPTIONAL parameter data type:

- Type String: the empty string ("").

- Type DateTime: "0001-01-01T00:00:00Z".

- Type Integer: "-1".

- Type EndUserIdentifier (which encapsulates a URI): "null://null".

## Document Structure

This document has the following sections:

- Introduction

- Common Data Definitions

- Third Party Call

- Network-Initiated Third Party Call

- SMS

- Multimedia Message

- Payment

- Account Management

- User Status

- Terminal Location

Annex A. Index of Parlay X API Messages

Apart from (this) section 1 and section 2, each of the remaining sections specifies a Parlay X Web Service with the following structure:

- Record of Changes, providing a detailed record of any additions, deletions, modifications and other changes that have been applied to the specification of the Web Service since its previous public release.

- Overview, describing the Web Service, the underlying commercial and/or technical rationale, its relationship to other specifications, and illustrative usage scenario(s).

- A semantic specification of the message-based Parlay X API(s) that constitute the Web Service.

- A definition of the Web-Service-specific data types and exceptions.

- Web Service Syntax, referencing two types of WSDL files  for this release of the Parlay X APIs:

- A modular set of WSDL files that provide an 'rpc/literal' binding and follows the current draft provided by the WS-I Basic Profile.  This set of files may be used by tools that support the features included in the Basic Profile definition.

- A second set of monolithic WSDL files that provide an 'rpc/encoded' binding and use SOAP encoded arrays.  This allows developers to use tools that do not yet support the features included in the Basic Profile definition.  It is expected that tools will be updated over time, and that developers will migrate to the first set of files, to be compliant with the WS-I Basic Profile.

This document structure, one section for each Parlay X Web Service, facilitates future releases of the Parlay X specification.  It minimizes the scope of editorial work required to either introduce a new Parlay X Web Service, which is accomplished by adding a new document section, or to update an existing Parlay X Web Service, which is achieved by editing a single, existing document section.

In addition to the Parlay X Web Service-specific sections, this document (in section 2) provides a listing of data definitions (including exceptions) that are common across multiple Parlay X Web Services.  As more Web Services are defined in the future, the number of common data definitions may increase.  Thus section 2 has the following structure:

- Record of Changes, providing a detailed record of any additions, deletions, modifications and other changes that have been applied to the data definitions since its previous public release.

- An English language definition of the common data types and exceptions.

- Common Data Definitions Syntax, referencing two types of WSDL files for this release of the Parlay X APIs.

# Common Data Definitions

## Record of Changes

This sub-section will be used in the future for tracking changes to version 1.0 (and any later versions) of the Common Data Definitions.  It will consist of three parts capturing changes to Data Types, Exceptions and ‘Others’, as appropriate.

## Common Data Type Definitions

Where possible standard XML Schema data types are used, as defined in http://www.w3.org/TR/xmlschema-2/#built-in-datatypes.

Other data types that are common to multiple Parlay X Web Services are defined in the following sub-sections.

EndUserIdentifier

The EndUserIdentifier data type is specified as a URI: [scheme]:[schemeSpecificPart] (RFC 2396, amended by RFC 2732). Example schemes are tel (RFC 2806) and sip (RFC 3261).

ArrayOfEndUserIdentifier

A collection of elements where each element is of data type EndUserIdentifier.

ArrayOfURI

A collection of elements where each element is of data type URI.

## Common Exception Definitions

All of these exceptions are common to multiple Parlay X Web Services. Each exception is assigned an eight character identifier, where:

- The first 3 characters “GEN” identify the exception as generic: i.e. common to multiple Parlay X services.  The “GEN” string shall not be assigned to any Parlay X Web Service-specific exception.

- The next 4 digits “1xxx” uniquely identifies the exception within the set of common exceptions. The “1xxx” string may be re-used by any Parlay X Web Service-specific exception defined in this specification.

- The last character identifies the severity of the exception condition, as follows:

- “F”: fatal error, typically indicating an infrastructure problem; the operation triggering the exception should not be retried

- “E”: error, typically indicating an application or user error; the operation triggering the exception has not completed and may be retried

- “W”: warning, typically indicating that an operation has completed, but there are cautions or other caveats.

The common exceptions are as follows:

| UNIQUE ID | TEXT STRING | MEANING |
| --- | --- | --- |
| GEN1000E | UnknownEndUserException | This fault occurs if the end user identification that is passed is unknown. |
| GEN1001E | InvalidArgumentException | This fault occurs if an argument passed is semantically incorrect or when the parameter does not conform to the limits specified in the Parlay X specification: e.g. when passing the end user identification: "tel:www.parlay.org". |
| GEN1002F | ServiceException | This fault is caused by generic platform or network errors. |
| GEN1003E | PolicyException | This fault is caused by a violation of a policy of the Parlay X Web Service: e.g., when parameter values are used that are outside the scope of the service level agreement. |
| GEN1004E | ApplicationException | This fault is caused by a generic error in an application web service when processing a message invocation from a Parlay X Web Service. The Parlay X Web Service can log this information and possibly raise an alarm when the number of exceptions reaches a pre-defined threshold. |
| GEN1005W | MessageTooLongException | This fault is caused if a message to be sent exceeds the maximum length supported by the Web Service; e.g. the message may be too long for a destination terminal device. |

## Common Data Definitions Syntax – WSDL

The rpc/literal files include two common files

- parlayx_common_types.xsd

- parlayx_common_faults.wsdl

The rpc/encoded files contain these definitions within each service file.

# Third Party Call

## Record of Changes

This sub-section will be used in the future for tracking changes to version 1.0 (and any later versions) of the Third Party Call Web Service.  It will consist of four parts capturing changes to Messages, Data Definitions, Exceptions and ‘Others’, as appropriate.

## Overview

Description

Currently, in order to perform a third party call in telecommunication networks we have to write applications using specific protocols to access Call Control functions provided by network elements (specifically operations to initiate a call from applications). This approach requires a high degree of network expertise. We can also use the OSA gateway approach, invoking standard interfaces to gain access to call control capabilities, but these interfaces are usually perceived to be quite complex by application IT developers. Developers must have advanced  telecommunication skills to use Call Control OSA interfaces.

In this section we describe a Parlay X Web Service, Third Party Call, for creating and managing a call initiated by an application (third party call). The overall scope of this Web Service is to provide functions to application developers to create a call in a simple way. Using the Third Party Call Web Service, application developers can invoke call handling functions without detailed telecommunication knowledge.

Commercial & Technical Rationale

The basic commercial rationale for developing the Third Party Call Web Service is:

to increase the use of Call Control capabilities in software applications

to empower traditional IT developers to produce large numbers of such applications

to lower the development cost and time for such applications.

Relationship to Similar or Supplanted Specifications

In the PSTN/Internet Interworking (PINT) working group a “request to call” scenario has been defined (RFC 2848). A request is sent to an IP host that cause a phone call to be made, connecting party A to some remote party B.

The PINT approach is not API-based but instead it proposes an extension to SIP to implement the scenarios identified. The Third Party Call Web Service proposed here while addressing similar scenarios aims at providing a high-level Web Services interface to invoke the service. It does not aim at defining a concrete architecture implementing the functionality. Therefore the two specifications are at different levels of abstraction.

Scenarios

Figure 2 shows an scenario using the Third Party Call Web Service to handle third party call functions. The application invokes a web service to retrieve stock quotes and a Parlay X Interface to initiate a third party call between a broker and his client.

In the scenario, whenever a particular stock quote reaches a threshold value (1) and (2), the client application invokes a third party call between one or more brokers and their corresponding customers to decide actions to be taken. After invocation (3) by the application, the Third Party Call Web Service invokes a Parlay API method (4) using the Parlay/OSA SCS-CC (Call control) interface. This SCS handles the invocation and sends a message (5) to an MSC to set-up a call between user A and user B.

In an alternative scenario, the Parlay API interaction involving steps (4) and (5) could be replaced with a direct  interaction between the Third Party Call Web Service and the Mobile network.

Figure 2: Third Party Call Scenario

## Call API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations are:

makeACall

getCallInformation

endCall

cancelCallRequest

Attempt Immediate Call Set-Up Between Two Addresses

makeACall(EndUserIdentifier callingParty, EndUserIdentifier calledParty, String charging, out String callIdentifier)

Behavior:

The invocation of makeACall requests to set-up a voice call between two addresses, callingParty and calledParty, provided that the invoking application is allowed to connect them. Optionally the application can also indicate the charging arrangements (charging), i.e. the name of an operator-specific charging plan that defines who to charge for the call and how much.

By invoking this operation the application requires to monitor the status of the requested call. The returned parameter, callIdentifier, can be used to identify the call.  In order to receive the information on call status the application has to explicitly invoke getCallInformation.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| callingParty | EndUserIdentifier | It contains the address of the first user involved in the call |
| calledParty | EndUserIdentifier | It contains the address of the second user involved in the call |
| charging | String | OPTIONAL. If present, represents the name of an operator-specific charging plan that defines who to charge for the call and how much. If the named charge plan does not exist, the InvalidArgumentException is thrown. If no charge plan is specified, charging occurs in accordance with an operator-specific charging policy. |
| callIdentifier | String | OUTPUT. It identifies a specific call request |

Exceptions:

UnknownEndUserException

InvalidArgumentException

ServiceException

Get Current Status of a Call

getCallInformation(String callIdentifier, out CallInformationType callInformation)

Behavior:

The invocation of getCallInformation retrieves the current status, callInformation, of the call identified by callIdentifier.  This method can be invoked multiple times by the application even if the call has already ended. However, after the call has ended, status information will be available only for a limited period of time that should be specified in an off-line configuration step.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| callIdentifier | String | It identifies a specific call request |
| callInformation | CallInformationType | OUTPUT. It identifies the status of the call |

Exceptions:

UnknownCallIdentifierException

ServiceException

End a Call

endCall(String callIdentifier)

Behavior:

The invocation of endCall terminates the call identified by callIdentifier. If the call is still in the initial state this method has the same effect as the cancelCallRequest method.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| callIdentifier | String | It identifies a specific call request |

Exceptions:

CallTerminatedException

UnknownCallIdentifierException

ServiceException

Cancel a Call Request

cancelCallRequest(String callIdentifier)

Behavior:

The invocation of cancelCallRequest cancels the previously requested call identified by callIdentifier. Note that this method differs from the endCall method since it only attempts to prevent the call from starting but it does not have any effect if the call has already started.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| callIdentifier | String | It identifies a specific call request |

Exceptions:

CallConnectedException

UnknownCallIdentifierException

ServiceException

## Web Service Data Definitions

Data Types

In addition to the Common Data Types defined in Section 2.2, the following Data Types are specific to this Web Service.

CallInformationType

The CallInformationType data type is a structure containing the following parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| callStatus | CallStatus | It indicates the current status of the call (see possible values below) |
| startTime | DateTime | When applicable (callStatus <> CallInitial), it indicates the time of the beginning of the call |
| duration | Integer | When applicable (callStatus = CallTerminated), it indicates the duration of the call expressed in seconds |
| terminationCause | CallTermination Cause | When applicable (callStatus = CallTerminated), it indicates the cause of the termination of the call (see possible values below) |

CallStatus

The CallStatus data type is an enumeration with the following values:

| VALUE | DESCRIPTION |
| --- | --- |
| CallInitial | The call is being established |
| CallConnected | The call is active |
| CallTerminated | The call was terminated |

CallTerminationCause

The CallTerminationCause data type is an enumeration with the following values:

| VALUE | DESCRIPTION |
| --- | --- |
| CallingPartyNoAnswer | Calling Party did not answer |
| CalledPartyNoAnswer | Called Party did not answer |
| CallingPartyBusy | Calling Party was busy |
| CalledPartyBusy | Called Party was busy |
| CallingPartyNotReachable | Calling Party was not reachable |
| CalledPartyNotReachable | Called Party was not reachable |
| CallHangUp | The call was terminated by either party hanging up |
| CallAborted | The call was aborted (any other termination cause) |

Exceptions

In addition to the Common Exceptions defined in Section 2.3, there are exceptions specific to this Web Service.  Similar to the Common Exceptions, each Web Service-specific exception is assigned an eight character identifier. This identifier is interpreted as described in Section 2.3, except that the first 3 characters uniquely identify this Web Service.

The following exceptions are specific to this Web Service:

| UNIQUE ID | TEXT STRING | MEANING |
| --- | --- | --- |
| 3PC1000W | CallConnectedException | The call was already active |
| 3PC1001W | CallTerminatedException | The call is already terminated |
| 3PC1002E | UnknownCallIdentifier Exception | The callIdentifier supplied does not relate to any known call request or has expired. |

## Web Service Syntax – WSDL

The rpc/literal files are

- parlayx_third_party_calling_types.xsd

- parlayx_third_party_calling_service_port.wsdl

- parlayx_third_party_calling_service.wsdl

The rpc/encoded file is

- parlayx_third_calling_party_service.wsdl.

# Network-Initiated Third Party Call

## Record of Changes

This sub-section will be used in the future for tracking changes to version 1.0 (and any later versions) of the Network-Initiated Third Party Call Web Service.  It will consist of four parts capturing changes to Messages, Data Definitions, Exceptions and ‘Others’, as appropriate.

## Overview

Description

Currently, in order to determine the handling of a subscriber initiated call in telecommunication networks we have to write applications using specific protocols to access Call Control functions provided by network elements. This approach requires a high degree of network expertise. We can also use the OSA gateway approach, invoking standard interfaces to gain access to call control capabilities, but these interfaces are usually perceived to be quite complex by application IT developers. Developers must have advanced telecommunication skills to use Call Control OSA interfaces.

In this section we will describe a Parlay X Web Service, Network-Initiated Third Party Call, for handling calls initiated by a subscriber in the network. A (third party) application determines how the call should be treated. The overall scope of this Web Service is to provide simple functions to application developers to determine how a call should be treated. Using the Network-Initiated Third Party Call Web Service, application developers can perform simple handling of network-initiated calls without specific Telco knowledge.

Commercial & Technical Rationale

The basic commercial rationale for developing the Network-Initiated Third Party Call Web Service is:

to increase the use of Call Control capabilities in software applications

to empower traditional IT developers to produce large numbers of such applications

to lower the development cost and time for such applications.

Relationship to Similar or Supplanted Specifications

All the capabilities of the Network-Initiated Third Party Call Web Service (and more) can also be achieved with the Parlay/OSA generic call control or multiparty call control services. The Network-Initiated Third Party Call Web Service can be seen as a very limited subset of the network initiated call control functionality present in Parlay/OSA. This has the advantage that the application needs less telecom knowledge. The disadvantage is that the control over the call is much reduced. Basically, a Parlay X application can only choose to release, continue or re-route the call. It does not have control over the specific parameters used in the call (e.g., on the presentation indicators of the addresses), nor can the application control the call over a longer period of time. Furthermore, it is not likely that the robustness and performance requirements of Parlay/OSA services will be matched by the Network-Initiated Third Party Call Web Service.

Scenarios

This section gives some possible scenarios using the Network-Initiated Third Party Call Web Service to handle network-initiated calls.

Incoming call handling

A subscriber receives a call while he is logged-on to the Internet. Since this occupies his telephone connection, he is regarded as busy by the network. The subscriber has an application that is invoked when somebody tries to call him while he is busy. The application provides the subscriber with a list of choices on how to handle the call (e.g., route the call to voicemail, redirect the call to a secretary, reject the call). Based on the response of the subscriber the call is handled in the network.

Alternatively, the call be re-routed or released depending on the preferences of the subscriber and some context information (e.g., based on the status or location of the subscriber).

Service numbers

An application is triggered whenever a certain service number is dialled. This number is used to connect the caller to one of the maintenance personnel. The application redirects the call to the appropriate maintenance person based on, e.g., calling party number, time, location and availability of the maintenance personnel.

## Call API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations are:

- handleBusy

- handleNotReachable

- handleNoAnswer

- handleCalledNumber

- handleOffHook

These messages are initiated by the Network-Initiated Third Party Call Web Service (running in a Parlay X Gateway) and invoke an application web service(s), as a result of activity in the network. The result of the invocation is used as an indication on how the call should be handled in the network.

Note that because the results of the invocations of the application web service(s) determine call handling in the network, the names of the methods are prefixed with ‘handle’, rather than ‘notify’. The prefix ‘notify’ would imply a more asynchronous behavior, whereas ‘handle’ shows the synchronous nature of these invocations.

The type of  events (busy, answer etc.) and related numbers, for which the application web service(s) should be invoked, should be determined by the operator in an off-line process.

Request Application Handling of a ‘Busy’ Condition

handleBusy(EndUserIdentifier callingParty, EndUserIdentifier calledParty, out Action action)

Behavior:

The invocation of handleBusy requests the application to inform the gateway how to handle the call between two addresses, the callingParty and the calledParty,  where the calledParty is busy when the call is received.  The application returns the action, which directs the gateway to perform one of the following actions:

- “Continue”, resulting in normal handling of the busy event in the network, e.g. playing of a busy tone to the callingParty

- “EndCall”, resulting in the call being terminated; the exact tone or announcement that will be played to the callingParty is operator-specific

- “Route”, resulting in the call being re-routed to a calledParty specified by the application.

Optionally, in the action parameter, the application can also indicate the charging arrangements, i.e. the name of an operator-specific charging plan that defines who to charge for the call and how much.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| callingParty | EndUserIdentifier | It contains the address of the caller. |
| calledParty | EndUserIdentifier | It contains the address of the called party. This party is busy. |
| action | Action | OUTPUT. It indicates the action to be performed by the gateway. |

Exceptions:

ApplicationException

UnknownEndUserException

InvalidArgumentException

Request Application Handling of a ‘Not Reachable’ Condition

handleNotReachable(EndUserIdentifier callingParty, EndUserIdentifier calledParty, out Action action)

Behavior:

The invocation of handleNotReachable requests the application to inform the gateway how to handle the call between two addresses, the callingParty and the calledParty, where the calledParty is not reachable when the call is received.  The application returns the action, which directs the gateway to perform one of the following actions:

- “Continue”, resulting in normal handling of the ‘not reachable’ event in the network, e.g. playing of a busy tone to the callingParty

- “EndCall”, resulting in the call being terminated; the exact tone or announcement that will be played to the callingParty is operator-specific

- “Route”, resulting in the call being re-routed to a calledParty specified by the application.

Optionally, in the action parameter, the application can also indicate the charging arrangements, i.e. the name of an operator-specific charging plan that defines who to charge for the call and how much.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| callingParty | EndUserIdentifier | It contains the address of the caller. |
| calledParty | EndUserIdentifier | It contains the address of the called party. This party is not reachable. |
| action | Action | OUTPUT. It indicates the action to be performed by the gateway. |

Exceptions:

ApplicationException

UnknownEndUserException

InvalidArgumentException

Request Application Handling of a ‘No Answer’ Condition

handleNoAnswer(EndUserIdentifier callingParty, EndUserIdentifier calledParty, out Action action)

Behavior:

The invocation of handleNoAnswer requests the application to inform the gateway how to handle the call between two addresses, the callingParty and the calledParty,  where the calledParty does not answer the received call. The application returns the action, which directs the gateway to perform one of the following actions:

- “Continue”, resulting in normal handling of the ‘no answer’ event in the network, e.g. playing of a busy tone to the callingParty

- “EndCall”, resulting in the call being terminated; the exact tone or announcement that will be played to the callingParty is operator-specific

- “Route”, resulting in the call being re-routed to a calledParty specified by the application.

Optionally, in the action parameter, the application can also indicate the charging arrangements, i.e. the name of an operator-specific charging plan that defines who to charge for the call and how much.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| callingParty | EndUserIdentifier | It contains the address of the caller. |
| calledParty | EndUserIdentifier | It contains the address of the called party. This party does not answer the call. |
| action | Action | OUTPUT. It indicates the action to be performed by the gateway. |

Exceptions:

ApplicationException

UnknownEndUserException

InvalidArgumentException

Request Application Handling of a ‘Called Number’ Condition

handleCalledNumber(EndUserIdentifier callingParty, EndUserIdentifier calledParty, out Action action)

Behaviour:

The invocation of handleCalledNumber requests the application to inform the gateway how to handle the call between two addresses, the callingParty and the calledParty.  The method is invoked when the callingParty tries to call the calledParty, but before the network routes the call to the calledParty. For example, the calledParty does not have to refer to a real end user, i.e., it could be a service number. The application returns the action, which directs the gateway to perform one of the following actions:

- “Continue”, resulting in normal handling in the network, i.e. the call will be routed to the calledParty number, as originally dialed

- “EndCall”, resulting in the call being terminated; the exact tone or announcement that will be played to the callingParty is operator-specific

- “Route”, resulting in the call being re-routed to a calledParty specified by the application.

Optionally, in the action parameter, the application can also indicate the charging arrangements, i.e. the name of an operator-specific charging plan that defines who to charge for the call and how much.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| callingParty | EndUserIdentifier | It contains the address of the caller. |
| calledParty | EndUserIdentifier | It contains the address of the called party. |
| action | Action | OUTPUT. It indicates the action to be performed by the gateway. |

Exceptions:

ApplicationException

UnknownEndUserException

InvalidArgumentException

Request Application Handling of an ‘Off Hook’ Condition

handleOffHook(EndUserIdentifier callingParty, out Action action)

Behaviour:

The invocation of handleOffHook requests the application to inform the gateway how to handle the fact that the callingParty tries to initiate a call. The application returns the action, which directs the gateway to perform one of the following actions:

- “Continue”, resulting in normal handling in the network, i.e. the calling party can enter digits and, when enough digits are entered, the call is routed based on this information

- “EndCall”, resulting in the call being terminated; the exact tone or announcement that will be played to the callingParty is operator-specific

- “Route”, resulting in the call being routed to a calledParty specified by the application.

Optionally, in the action parameter, the application can also indicate the charging arrangements, i.e. the name of an operator-specific charging plan that defines who to charge for the call and how much.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| callingParty | EndUserIdentifier | It contains the address of the caller. |
| action | Action | OUTPUT. It indicates the action to be performed by the gateway. |

Exceptions:

ApplicationException

UnknownEndUserException

InvalidArgumentException

## Web Service Data Definitions

Data Types

In addition to the Common Data Types defined in Section 2.2, the following Data Types are specific to this Web Service.

Action

The Action data type is a structure containing the following parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| actionToPerform | ActionValues | Indicates the action as described below |
| routingAddress | EndUserIdentifier | The address to be used in case the action indicates ‘Route’ |
| charging | String | OPTIONAL. If present, represents the name of an operator-specific charging plan that defines who to charge for the call and how much. If no charge plan is specified, the charging will be based on an operator-specific charging policy. |

ActionValues

The ActionValues data type is an enumeration with the following values:

| VALUE | DESCRIPTION |
| --- | --- |
| Route | Request to (re-)route the call to the address indicated with routingAddress. |
| Continue | Request to continue the call without any changes. This will result in normal handling of the event in the network |
| EndCall | Request to end the call. This will result in termination of the call. The callingParty will receive a tone or announcement. |

Exceptions

All exceptions thrown by this Web Service are Common Exceptions, as defined in Section 2.3.

## Web Service Syntax – WSDL

The rpc/literal files are

- parlayx_network_initiated_call_types.xsd

- parlayx_network_initiated_call_service_port.wsdl

- parlayx_network_initiated_call_service.wsdl

The rpc/encoded file is

- parlayx_network_initiated_call_service.wsdl.

# SMS

## Record of Changes

This sub-section will be used in the future for tracking changes to version 1.0 (and any later versions) of the SMS Web Service.  It will consist of four parts capturing changes to Messages, Data Definitions, Exceptions and ‘Others’, as appropriate.

## Overview

Description

Currently, in order to programmatically receive and send SMS it is necessary to write applications using specific protocols to access SMS functions provided by network elements (e.g., SMS-C). This approach requires a high degree of network expertise. Alternatively it is possible to use the Parlay/OSA approach, invoking standard interfaces (e.g., User Interaction or Messaging Service Interfaces) to gain access to SMS capabilities, but these interfaces are usually perceived to be quite complex by IT application developers. Developers must have advanced  telecommunication skills to use OSA interfaces.

In this chapter we describe a Parlay X Web Service, SMS for sending and receiving SMS. The overall scope of this Web Service is to provide to application developers primitives to handle SMS in a simple way. In fact, using the SMS Web Service, application developers can invoke SMS functions without specific Telco knowledge.

For sending a message to the network (reference 5.3, Send SMS API), the application invokes a message to send it and must subsequently become active again to poll for delivery status.  There is an alternative to this polling mechanism, i.e. an asynchronous notification mechanism implemented with an application-side web service.  However it was decided not to provide a notification mechanism in the first release, to make the API as simple as possible, even though the polling mechanism is not as network efficient as the notification mechanism.

For receiving a message from the network, the application may use either polling (reference section 5.5, Receive SMS API) or notification (reference section 5.4, SMS Notification API) mechanisms. The notification mechanism is more common: network-initiated messages are sent to autonomous application-side web services. Both mechanisms are supported, but the provisioning of the notification-related criteria is not specified.

Commercial & Technical Rationale

The basic commercial rationale for developing the SMS Web Service is:

to increase the use of SMS capabilities in software applications

to empower traditional IT developers to produce large numbers of such applications

to lower the development cost and time for such applications.

Relationship to Similar or Supplanted Specifications

Published web services exist that allow transmission of SMS messages, ring-tones and operator logos. For example, the Xmethods site (http://www.xmethods.com/) hosts more than one web service to handle SMS. These web services provide basic SMS capabilities, each using a different interfaces. The SMS Web Service aims to be a standard way to perform SMS operations and to provide more advanced features.

To specify the format of logos and ringtones, the following alternatives exist:

- ETSI/3GPP EMS format.

- Nokia’s Smart Messaging format.

- Other proprietary formats

Both the standardized EMS format and de facto Smart Messaging formats are supported. As an enhancement to SMS for sending content, dedicated methods are proposed taking into account the different content formats applied on the market.

Scenarios

Figure 3 shows a scenario using the SMS Web Service to send an SMS message from an application. The application invokes a web service to retrieve a weather forecast for a subscriber (1) & (2) and a Parlay X Interface (3) to use the SMS Web Service operations (i.e. to send an SMS). After invocation, the SMS Web Service invokes a Parlay API method (4) using the Parlay/OSA SCS-SMS (User Interaction) interface. This SCS handles the invocation and sends an UCP operation (5) to an SMS-C.  Subsequently the weather forecast is delivered (6) to the subscriber.

In an alternative scenario, the Parlay API interaction involving steps (4) and (5) could be replaced with a direct  interaction between the SMS Web Service and the Mobile network.

Figure 3: Send SMS Scenario

Figure 4 shows a scenario using the SMS Web Service to deliver a received SMS message to an application. The application receives a Parlay X web service invocation to retrieve an SMS sent by a subscriber (1) & (2). The SMS message contains the e-mail address of the person the user wishes to call.  The application invokes a Parlay X Interface (3) to the Third Party Call Web Service in order to initiate the call (4).

Figure 4: Receive SMS Scenario

## Send SMS API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations (i.e. of the SMS Web Service by the application) are:

sendSms

sendSmsLogo

sendSmsRingtone

getSmsDeliveryStatus.

Send an SMS Message

sendSms (EndUserIdentifier[] destinationAddressSet, String senderName, String charging, String message, out String requestIdentifier)

Behavior:

The invocation of sendSms requests to send an SMS, specified by the String message to the specified address (or address set), specified by destinationAddressSet. Optionally the application can also indicate the sender name (senderName), i.e. the string that is displayed on the user’s terminal as the originator of the message, and the charging arrangements (charging), i.e. the name of an operator-specific charging plan that defines who to charge for the SMS and how much. By invoking this operation the application requires to receive the notification of the status of the SMS delivery. In order to receive this information the application has to explicitly invoke the getSmsDeliveryStatus.  The requestIdentifier, returned by the invocation, can be used to identify the SMS delivery request.

For GSM systems, if message contains characters not in the GSM 7-bit character set, the SMS is sent as a Unicode SMS.

If message is longer than the maximum supported length (e.g. for GSM, 160 GSM 7-bit characters or 70 Unicode characters), the message will be sent as several concatenated short messages.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| destinationAddressSet | Array of EndUserIdentifier | Addresses to which the SMS will be sent |
| senderName | String | If present, it indicates the SMS sender name, i.e. the string that is displayed on the user’s terminal as the originator of the message. |
| charging | String | OPTIONAL. If present, represents the name of an operator-specific charging plan that defines who to charge for the SMS and how much. If the named charge plan does not exist, the InvalidArgumentException is thrown. If no charge plan is specified, the sending service/application will be charged, based on an operator-specific charging policy. |
| message | String | Text to be sent in SMS |
| requestIdentifier | String | OUTPUT. It identifies a specific SMS delivery request |

Exceptions:

UnknownEndUserException

InvalidArgumentException

ServiceException

MessageTooLongException

PolicyException

Send an SMS Logo

sendSmsLogo(EndUserIdentifier[] destinationAddressSet, String senderName, String charging, Base64Binary image, SmsFormat smsFormat, out String requestIdentifier)

Behavior:

The invocation of sendSmsLogo requests to send an SMS logo, specified by the byte array image to the specified address (or address set), specified by destinationAddressSet. Optionally the application can also indicate the sender name (senderName), i.e. the string that is displayed on the user’s terminal as the originator of the message, and the charging arrangements (charging), i.e. the name of an operator-specific charging plan that defines who to charge for the SMS logo and how much. By invoking this operation the application requires to receive the notification of the status of the SMS delivery. In order to receive this information the application has to explicitly invoke the getSmsDeliveryStatus.  The requestIdentifier, returned by the invocation, can be used to identify the SMS delivery request.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| destinationAddressSet | Array of EndUserIdentifier | Addresses to which the SMS logo will be sent |
| senderName | String | If present, it indicates SMS sender name, i.e. the string that is displayed on the user’s terminal as the originator of the message. |
| charging | String | OPTIONAL. If present, represents the name of an operator-specific charging plan that defines who to charge for the SMS logo and how much. If the named charge plan does not exist, the InvalidArgumentException is thrown. If no charge plan is specified, the sending service/application will be charged, based on an operator-specific charging policy. |
| image | Base64Binary | The image in jpeg, gif or png format. The image will be scaled to the proper format. |
| smsFormat | SmsFormat | Possible values are: ‘Ems’, ‘SmartMessaging’. |
| requestIdentifier | String | OUTPUT. It identifies a specific SMS delivery request |

Exceptions:

UnknownEndUserException

InvalidArgumentException

MessageTooLongException

UnsupportedFormatException

ServiceException

PolicyException

Send an SMS Ringtone

sendSmsRingtone(EndUserIdentifier[] destinationAddressSet, String senderName, String charging, String ringtone, SmsFormat smsFormat, out String requestIdentifier)

Behavior:

The invocation of sendSmsRingtone requests to send an SMS ringtone, specified by the String ringtone (in RTX format) to the specified address (or address set), specified by destinationAddressSet. Optionally the application can also indicate the sender name (senderName) i.e. the string that is displayed on the user’s terminal as the originator of the message, and the charging arrangements (charging), i.e. the name of an operator-specific charging plan that defines who to charge for the SMS ringtone and how much. By invoking this operation the application requires to receive the notification of the status of the SMS delivery. In order to receive this information the application has to explicitly invoke the getSmsDeliveryStatus.  The requestIdentifier, returned by the invocation, can be used to identify the SMS delivery request.

Depending on the length of the ringtone, it may be sent as several concatenated short messages.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| destinationAddressSet | Array of EndUserIdentifier | Addresses to which the SMS ringtone will be sent |
| senderName | String | If present, it indicates SMS sender name, i.e. the string that is displayed on the user’s terminal as the originator of the message. |
| charging | String | OPTIONAL. If present, represents the name of an operator-specific charging plan that defines who to charge for the SMS ringtone and how much. If the named charge plan does not exist, the InvalidArgumentException is thrown. If no charge plan is specified, the sending service/application will be charged, based on an operator-specific charging policy. |
| ringtone | String | The ringtone in RTX format. (http://www.logomanager.co.uk/help/Edit/RTX.html) |
| smsFormat | SmsFormat | Possible values are: ‘Ems’, ‘SmartMessaging’. |
| requestIdentifier | String | OUTPUT. It identifies a specific SMS delivery request |

Exceptions:

UnknownEndUserException

InvalidArgumentException

UnsupportedFormatException

MessageTooLongException

ServiceException

PolicyException

Get Current Status of an SMS Delivery

getSmsDeliveryStatus(String requestIdentifier, out DeliveryStatusType[] deliveryStatus)

Behavior:

The invocation of getSmsDeliveryStatus requests the status of a previous SMS delivery request identified by requestIdentifier. The information on the status is returned in deliveryStatus, which is an array of status related to the request identified by requestIdentifier. The status is identified by a couplet indicating a user address and the associated delivery status. This method can be invoked multiple times by the application even if the status has reached a final value. However, after the status has reached a final value, status information will be available only for a limited period of time that should be specified in an off-line configuration step. The following four different SMS delivery status have been identified:

- ‘Delivered’: in case of concatenated messages, only when all the SMS-parts have been successfully delivered.

- ‘DeliveryUncertain’:  e.g. because it was handed off to another network.

- ‘DeliveryImpossible’: unsuccessful delivery; the message could not be delivered before it expired.

- ‘MessageWaiting’: the message is still queued for delivery.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| requestIdentifier | String | It identifies a specific SMS delivery request |
| deliveryStatus | Array of DeliveryStatusType | OUTPUT. It lists the variations on the delivery status of the SMS |

Exceptions:

UnknownRequestIdentifierException

ServiceException

## SMS Notification API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations (i.e. of anotification web service by the SMS Web Service) are:

- notifySmsReception

Notify Application of an SMS Message Sent to a Specific Address

notifySmsReception(String registrationIdentifier, String smsServiceActivationNumber, EndUserIdentifier senderAddress, String message)

Behavior:

The notifySmsReception method must be implemented by a Web Service at the application side. It will be invoked by the Parlay X server to notify the application of the reception of an SMS. The notification will occur if and only if the SMS received fulfills the criteria specified in an off-line provisioning step, identified by the registrationIdentifier. The criteria must at least include an smsServiceActivationNumber, i.e. the SMS destination address that can be "monitored" by the application. The parameter senderAddress contains the address of the sender. The application can apply the appropriate service logic to process the SMS.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| registrationIdentifier | String | Identifies the off-line provisioning step that enables the application to receive notification of SMS reception according to specified criteria. |
| smsServiceActivation Number | String | Number associated with the invoked Message service, i.e. the destination address used by the terminal to send the message. |
| senderAddress | EndUserIdentifier | It indicates the address sending the SMS |
| message | String | Text received in the SMS |

Exceptions:

ApplicationException

## Receive SMS API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations (i.e. of the SMS Web Service by the application) are:

getReceivedSms.

Retrieve All SMS Messages Sent to a Specific Address

getReceivedSms(String registrationIdentifier, out SmsType[] receivedSms)

Behavior:

The invocation of getReceivedSms retrieves all the SMS messages received that fulfill the criteria identified by registrationIdentifier. The method returns only the list of SMS messages received since the previous invocation of the same method, i.e. each time the method is executed the messages returned are removed from the server. Moreover, each SMS message will be automatically removed from the server after a maximum time interval specified in an off-line configuration step.

The received SMS messages are returned in receivedSms. An SMS message is identified by a structure indicating the sender of the SMS message and the content.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| registrationIdentifier | String | Identifies the off-line provisioning step that enables the application to receive notification of SMS reception according to specified criteria. |
| receivedSms | Array of SmsType | OUTPUT. It lists the received SMS since last invocation. |

Exceptions:

UnknownRegistrationIdentifierException

ServiceException

## Web Service Data Definitions

Data Types

In addition to the Common Data Types defined in Section 2.2, the following Data Types are specific to this Web Service.

DeliveryStatusType

The DeliveryStatusType data type is a structure containing the following parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| destinationAddress | EndUserIdentifier | It indicates the destination address to which the notification is related |
| deliveryStatus | DeliveryStatus | Indicates the delivery result for destinationAddress. Possible values are: ‘Delivered’, ‘DeliveryUncertain’, ‘DeliveryImpossible’. |

DeliveryStatus

The DeliveryStatus data type is an enumeration with the following values:

| VALUE | DESCRIPTION |
| --- | --- |
| Delivered | Successful delivery |
| DeliveryUncertain | Delivery status unknown: e.g. because it was handed off to another network. |
| DeliveryImpossible | Unsuccessful delivery; the message could not be delivered before it expired. |
| MessageWaiting | The message is still queued for delivery. This is a temporary state, pending transition to one of the preceding states. |

SmsType

The SmsType data type is a structure containing the following parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| message | String | Text received in SMS |
| senderAddress | EndUserIdentifier | It indicates address sending the SMS |

SmsFormat

The SmsFormat data type is an enumeration with the following values:

| VALUE | DESCRIPTION |
| --- | --- |
| Ems | Enhanced Messaging Service, standardized in 3GPP TS 23.040, which defines a logo/ringtone format |
| SmartMessaging | Nokia’s de facto standard, which defines a logo/ringtone format |

Exceptions

In addition to the Common Exceptions defined in Section 2.3, there are exceptions specific to this Web Service.  Similar to the Common Exceptions, each Web Service-specific exception is assigned an eight character identifier. This identifier is interpreted as described in Section 2.3, except that the first 3 characters uniquely identify this Web Service.

The following exceptions are specific to this Web Service:

| UNIQUE ID | TEXT STRING | MEANING |
| --- | --- | --- |
| SMS1000E | UnsupportedFormatException | The smsFormat supplied is not one of the permitted values of the SmsFormat data type. |
| SMS1001E | UnknownRegistration IdentifierException | The registrationIdentifier supplied is not known by the server |
| SMS1002E | UnknownRequestIdentifier Exception | The requestIdentifier supplied does not relate to any known SMS request or has expired. |

## Web Service Syntax – WSDL

The rpc/literal files are

- parlayx_sms_types.xsd

- parlayx_sms_service_port.wsdl

- parlayx_sms_send_service.wsdl

- parlayx_sms_receive_service.wsdl

- parlayx_sms_notification_service_port.wsdl

- parlayx_sms_notification_service.wsdl

The rpc/encoded files are

- parlayx_sms_service.wsdl

- parlayx_sms_notification_service.wsdl

# Multimedia Message

## Record of Changes

This sub-section will be used in the future for tracking changes to version 1.0 (and any later versions) of the Multimedia Message Web Service.  It will consist of four parts capturing changes to Messages, Data Definitions, Exceptions and ‘Others’, as appropriate.

## Overview

Description

Currently, in order to programmatically receive and send Multimedia Messages, it is necessary to write applications using specific protocols to access MMS functions provided by network elements (e.g., MMS-C). This approach requires application developers to have a high degree of network expertise.

This contribution defines a Multimedia Message Web Service that can map to SMS, EMS,  MMS, IM, E-mail etc.

The choice is between defining one set of APIs per messaging network or a single set common to all networks; e.g. we could define sendMMS, sendEMS, sendSMS, … or just use sendMessage. Although the more specific the API the easier it is to use, there are advantages to a single set of  network-neutral APIs.  These advantages include:

- improved service portability

- lower complexity, by providing support for generic user terminal capabilities only.

For this version of the Parlay X specification, we provide sets of APIs for two messaging web services: SMS-specific APIs (as described in section 5) and Multimedia Message APIs (this section), which provides generic messaging features (including SMS).

For sending a message to the network (reference 6.3, Send Message API), the application invokes a message to send it and must subsequently become active again to poll for delivery status.  There is an alternative to this polling mechanism, i.e. an asynchronous notification mechanism implemented with an application-side web service.  However it was decided not to provide a notification mechanism in the first release, to make the API as simple as possible, even though the polling mechanism is not as network efficient as the notification mechanism.

For receiving a message from the network, the application may use either polling (reference section 6.4, Receive Message API) or notification (reference section 6.5, Message Notification API) mechanisms. The notification mechanism is more common: network-initiated messages are sent to autonomous application-side web services. Both mechanisms are supported, but the provisioning of the notification-related criteria is not specified.

Commercial & Technical Rationale

The scope of this Web Service is much more than an enhancement of the Parlay X SMS Web Service. The purpose is not to add more SMS features, but to form a generic multimedia adapted messaging API. The reason to incorporate SMS in the API is mainly to create one set of APIs for messaging instead of one set per network. We believe that the benefits of a single set of APIs, i.e. service portability and the ability to serve different handsets or even multiple sub-networks using common APIs, is highly beneficial for both the Network Operators and the Service Providers.

Relationship to Similar or Supplanted Specifications

This Web Service includes functions implemented in the SMS Web Service.

Scenarios

Figure 5 shows an example scenario using sendMessage and getMessageDeliveryStatus  to send data to subscribers and to determine if the data has been received by the subscriber. The application invokes a web service to retrieve a stock quote (1) & (2) and sends the current quote - sendMessage - using the Parlay X Interface (3) of the Multimedia Message Web Service. After invocation, the Multimedia Message Web Service sends the message to an MMS-C using the MM7 interface (4) for onward transmission (5) to the subscriber over the Mobile network

Later, when the next quote is ready, the application checks to see - getMessageDeliveryStatus - if the previous quote has been successfully delivered to the subscriber.  If not, it may for instance perform an action (not shown) to provide a credit for the previous message transmission. This way, the subscriber is only charged for a stock quote if it is delivered on-time.

Figure 5: Multimedia Messaging Scenario

## Send Message API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations (i.e. of the Multimedia Message Web Service by the application) are:

- sendMessage

- getMessageDeliveryStatus

Send a Multimedia Message

sendMessage(EndUserIdentifier [] destinationAddressSet, String senderAddress, String subject, MessagePriority priority, String charging, out String requestIdentifier) 	Attachment[content]

Behavior:

Request to send a Message to a set of destination addresses, returning a requestIdentifier to identify the message. The requestIdentifier can subsequently be used by the application to poll for the message status, i.e. using getMessageDeliveryStatus to see if the message has been delivered or not. The content is sent as a SOAP-Attachment encoded using MIME or DIME.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| destinationAddressSet | Array of EndUserIdentifier | Destination addresses for the Message. |
| senderAddress | String | OPTIONAL. If present, indicates Message sender address. This parameter is not allowed for all 3rd party providers. Parlay X server needs to handle this according to a SLA for the specific application and its use can therefore result in a PolicyException. |
| subject | String | OPTIONAL. If present, it indicates the message subject. If mapped to SMS this parameter will be used as the senderAddress, even if a separate senderAddress is provided. |
| priority | MessagePriority | OPTIONAL. If present, represents the priority of the message. If not defined, the network will assign a priority based on an operator policy. |
| charging | String | OPTIONAL. If present, represents the name of an operator-specific charging plan that defines who to charge for the message and how much. If the named charge plan does not exist, the InvalidArgumentException is thrown. If no charge plan is specified, the sending service/application will be charged, based on operator-specific charging policy. |
| requestIdentifier | String | OUTPUT. It is a correlation identifier that is used in a getMessageDeliveryStatus message invocation, i.e. to poll for the delivery status of all of the sent Messages. |
| Input Attachments |
| content | MIME or DIME format | Data to be sent with Message, i.e. in MIME or DIME format and sent as a SOAP-Attachment |

Exceptions

UnknownEndUserException

InvalidArgumentException

ServiceException

PolicyException

MessageTooLongException

Get Current Status of a Multimedia Message Delivery

getMessageDeliveryStatus(String requestIdentifier, out DeliveryStatusType[] deliveryStatus)

Behavior:

This is a poll method used by the application to retrieve delivery status for each message sent as a result of a previous sendMessage message invocation. The requestIdentifier parameter identifies this previous message invocation.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| requestIdentifier | String | Identifier related to the delivery status request. |
| deliveryStatus | Array of DeliveryStatusType | OUTPUT. It is an array of status of the messages that were previously sent. Each array element represents a sent message: i.e. its destination address and its delivery status. |

Exceptions

InvalidArgumentException

ServiceException

Policy Exception

UnknownRequestIdentifierException

## Receive Message API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations (i.e. of the Multimedia Message Web Service by the application) are:

- getReceivedMessages

- getMessageURIs

- getMessage

Provide Application with Multimedia Messages Sent to the Application

getReceivedMessages(String registrationIdentifier, MessagePriority priority, out MessageRef [] messageRef)

Behavior:

This method enables the application to poll for new messages associated with a specific registrationIdentifier. If the registrationIdentifier is not specified, the Parlay X server will return references to all messages sent to the application. The process of binding different registrationIdentifier parameters to applications is an off-line process. The Parlay X gateway shall not allow an application to poll for messages using registrationIdentifier parameters that are not associated with the application. The priority parameter may be used by the application to retrieve references to higher priority messages, e.g. if Normal is chosen only references to high priority and normal priority messages are returned. If the priority parameter is omitted all message references are returned.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| registrationIdentifier | String | Identifies the off-line provisioning step that enables the application to receive notification of Message reception according to specified criteria. |
| priority | MessagePriority | OPTIONAL. The priority of the messages to poll from the Parlay X gateway. All messages of the specified priority and higher will be retrieved. If not specified, all messages shall be returned, i.e. the same as specifying Low. |
| messageRef | Array of MessageRef | OUTPUT. It contains an array of messages received according to the specified filter of registrationIdentifier and priority. |

Exceptions

InvalidArgumentException

ServiceException

PolicyException

UnknownRegistrationIdentifierException

Retrieve URI References to the Parts of a Multimedia Message

getMessageURIs(String messageRefIdentifier, out MessageURI message)

Behavior:

This method will read the different parts of the message, create local files in the Parlay Gateway and return URI references to them. The application can then simply read each file or just have them presented as links to the end-user. The URIs to the files will be active for an agreed time.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| messageRefIdentifier | String | The identity of the message to retrieve. |
| message | MessageURI | OUTPUT. It contains the complete message, i.e. the textual part of the message, if such exists, and a list of file references for the message attachments, if any. |

Exceptions

InvalidArgumentException

ServiceException

PolicyException

UnknownMessageException

Provide Application with a Multimedia Message as an Attachment

getMessage(String messageRefIdentifier)   Attachments[out content]

Behavior:

This method will read the whole message. The data is returned as a SOAP-Attachment in the return message.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| messageRefIdentifier | String | The identity of the message |
| Output Attachments |
| content | MIME or DIME format | Data to be returned with Message, i.e. in MIME or DIME format and received as a SOAP-Attachment |

Exceptions

InvalidArgumentException

ServiceException

PolicyException

UnknownMessageException

## Message Notification API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations (i.e. of anotification web service by the Multimedia Message Web Service) are:

- notifyMessageReception

Notify Application of a Multimedia Message Sent to a Specific Address

notifyMessageReception (String registrationIdentifier, MessageRef messageRef)

Behavior:

This method will have to be implemented by a web service on the client application side. The registration of the URI for this application web service is done off-line.  This means that there is a registration mechanism in the Parlay X Gateway that binds different registrationIdentifier parameters to applications and their web service URIs.

A client application is notified that a new Message, sent to a specific Service Activation Number, has been received. Using the registrationIdentifier, the client application can apply appropriate service logic with specific behaviour.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| registrationIdentifier | String | A handle connected to the off-line registration of the notifications. This distinguishes registrations that point to the same application web service. |
| messageRef | MessageRef | This parameter contains all the information associated with the received message. |

Exceptions

ApplicationException

## Web Service Data Definitions

Data Types

In addition to the Common Data Types defined in Section 2.2, the following Data Types are specific to this Web Service.

MessagePriority

The MessagePriority data type is an enumeration with the following values:

| VALUE | DESCRIPTION |
| --- | --- |
| Default | This is the “NULL” value as described in section 1.6. This value is applicable if the parameter of type MessagePriority is tagged OPTIONAL. |
| Low | Low message priority |
| Normal | Normal message priority |
| High | High message priority |

DeliveryStatus

The DeliveryStatus data type is an enumeration with the following values:

| VALUE | DESCRIPTION |
| --- | --- |
| Delivered | Successful delivery |
| DeliveryUncertain | Delivery status unknown: e.g. because it was handed off to another network. |
| DeliveryImpossible | Unsuccessful delivery; the message could not be delivered before it expired. |
| MessageWaiting | The message is still queued for delivery. This is a temporary state, pending transition to one of the preceding states. |

DeliveryStatusType

The DeliveryStatusType data type is a structure containing the following parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| destinationAddress | EndUserIdentifier | Address associated with the delivery status. The address field is coded as a URI. |
| deliveryStatus | DeliveryStatus | Parameter indicating the delivery status. |

MessageRef

The MessageRef data type is a structure containing six parameters as described below.

This data type is used to return the basic message data when polled by the application.

- If a message is a pure text message, the content will be returned in the message parameter and the messageRefIdentifier parameter will then not be sent.

- If a message contains attachments or other non-text messages the message parameter will not be sent; instead the messageRefIdentifier will contain a reference to the message stored in the Parlay X gateway.

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| messageRefIdentifier | String | OPTIONAL: If present, contains a reference to a message stored in the Parlay X gateway. If the message is pure text, this parameter is not present. |
| messageService ActivationNumber | String | Number associated with the invoked Message service, i.e. the destination address used by the terminal to send the message. |
| senderAddress | EndUserIdentifier | Indicates message sender address |
| subject | String | OPTIONAL: If present, indicates the subject of the received message. This parameter will not be used for SMS services. |
| priority | MessagePriority | The priority of the message: default is Normal |
| message | String | OPTIONAL: If present, then the messageRefIdentifier is not present and this parameter contains the whole message. The type of the message is always pure ASCII text in this case. The message will not be stored in the Parlay X gateway. |

MessageURI

The MessageURI data type is a structure containing the following parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| bodyText | String | Contains the message body if it is encoded as ASCII text. |
| fileReferences | Array of URI | This is an array of URI references to all the attachments in the Multimedia message. These are URIs to different files, e.g. GIF pictures or pure text files. |

Exceptions

In addition to the Common Exceptions defined in Section 2.3, there are exceptions specific to this Web Service.  Similar to the Common Exceptions, each Web Service-specific exception is assigned an eight character identifier. This identifier is interpreted as described in Section 2.3, except that the first 3 characters uniquely identify this Web Service.

The following exceptions are specific to this Web Service:

| UNIQUE ID | TEXT STRING | MEANING |
| --- | --- | --- |
| MMM1000E | UnknownRequestIdentifier Exception | The Parlay X gateway did not recognize the requestIdentifier parameter. The message may have timed out or may have never been sent. This fault includes a string that provides additional information |
| MMM1001E | UnknownRegistration IdentifierException | The provided registration identifier does not exist. This fault includes a string that provides additional information. |
| MMM1002E | UnknownMessageException | The provided messageRefIdentifier was not found in the Parlay X gateway. The message may have been timed out or it may never have been received by the gateway. This fault includes a string that provides additional information |

## Web Service Syntax – WSDL

The rpc/literal files are

- parlayx_mm_types.xsd

- parlayx_mm_service_port.wsdl

- parlayx_mm_send_service.wsdl

- parlayx_mm_receive_service.wsdl

- parlayx_mm_notification_service_port.wsdl

- parlayx_mm_notification_service.wsdl

The rpc/encoded file is

- parlayx_mm_service.wsdl

- parlayx_mm_notification_service.wsdl

# Payment

Copyright © The Parlay Group, Inc.. All Rights Reserved. Copyright © PayCircle, Inc.. All Rights Reserved. This section of the document and translations of it, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, provided that the above copyright notice and this paragraph are included on all such copies and derivative works. However, this section of the document itself may not be modified in any way, such as by removing the copyright notice or references to The Parlay Group, and/or PayCircle, except as jointly determined by The Parlay Group and PayCircle. The limited permissions granted above are perpetual and will not be revoked by The Parlay Group, PayCircle, or their successors or assigns. This section of the document and the information contained herein is provided on an "AS IS" basis and The Parlay Group and PayCircle DISCLAIM ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE." The Parlay Group and PayCircle take no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this section of the document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. About PayCircle PayCircle is a non-profit organization represents more than 30 companies, including CSG Systems, Hewlett-Packard, Oracle, Siemens and Sun Microsystems as PayCircle Board Members. PayCircle membership is open to anyone who is active in the mobile payment market such as application developers, payment service providers, merchants, content providers, manufacturers of payment systems, suppliers for mobile infrastructure and mobile devices, network operators, banks, credit card companies, and others. The PayCircle consortium was formed January 2002 to define standard APIs for mobile payments, regardless of the payment systems used by application or service providers. This open approach guarantees that the necessary interfaces can be developed in a cooperative manner. The current list of members and additional information about the consortium and consortium membership is available at www.paycircle.org For additional information on PayCircle please contact: Stefan Schneiders, PayCircle Chief Operations Officer mailto:stefan.schneiders@siemens.com Tel: +49-89-636-53606

## Record of Changes

This sub-section will be used in the future for tracking changes to version 1.0 (and any later versions) of the Payment Web Service.  It will consist of four parts capturing changes to Messages, Data Definitions, Exceptions and ‘Others’, as appropriate.

## Overview

Description

A vast amount of content, both information and entertainment, will be made available to subscribers.  To support a business model that enables operators to offer integrated billing, a payment API is crucial.  We believe that open and inter-operable "payment APIs" are the key to market growth and investment protection.  The Payment Web Service supports payments for any content in an open, Web-like environment.

The Payment Web Service described in this document supports payment reservation, pre-paid payments, and post-paid payments.  It supports charging of both volume and currency amounts, a conversion function and a settlement function in case of a financially resolved dispute.

Note that certain parameters are negotiated off line.  For example the currency, volume type, default reservation enforcement time, as well as the taxation procedures and parameters.

Commercial & Technical Rationale

The payment process is a complex and critical component of telecom networks.  The Payment Web Service:

- further enlarges the market for third party software, services and content by providing essential primitives for integrated billing

- enables charging through trusted and authenticated service or content providers

- allows charging by subscriber address (e.g. MSISDN), against an existing reservation or directly against an account.

Relationship to Similar or Supplanted Specifications

Payment APIs are the focus of a number of industry standardisation initiatives:

- Parlay/OSA have developed powerful, carrier-grade Content-Based Charging (CBC) APIs

- PayCircle intends to provide a full, hand-crafted XML version of the Parlay/OSA CBC APIs

- Within the JCP, the JPay expert group seeks to specify a local Java API that can be implemented on top of either Parlay/OSA CBC, Parlay X Payment Web Service, or PayCircle's Payment Web Service

- OMA is commencing an e-commerce initiative.

The Payment Web Service provides a simpler, higher-level, WSDL-defined interface consistent with the Parlay X philosophy.

Scenarios

This section discusses two scenarios: one where the subscriber account is directly charged and one where a subscriber uses a service for which the provider needs a reservation. Note, associated Payment API messages are shown in ‘bold’ format: e.g. (chargeAmount).

Scenario #1:

Assume a subscriber is interested in downloading a ring tone to his mobile (MS).  The subscriber selects a ring tone and establishes a trusted relation with the ring tone provider.  Essentially, the ring tone provider obtains the address (MSISDN) and other information from the subscriber.  The ring tone may be downloaded to the MS using SMS.  As soon as the download succeeds, the provider of the ring tone will charge the subscriber (chargeAmount).

Scenario #2:

Assume a subscriber is interested in receiving a stream of, say, a soccer match.  The subscriber selects a match and establishes a trusted relation with the provider.  Again, the provider obtains the MSISDN and other information from the subscriber.  The subscriber wants to know what the service will cost and the provider interacts with the operators rating engine (getAmount) taking into account the subscriber's subscription, time of day, etc.  The value returned is a currency amount and is printed on the page that is displayed at the MS.  The subscriber then decides to stream the match to his MS.  Subsequently, the provider will reserve the appropriate amount with the operator (reserveAmount) to ensure that the subscriber can fulfil his payment obligations.  The match starts and the provider periodically charges against the reservation (chargeReservation).  The match ends in a draw and is extended with a 'sudden death' phase.  The subscriber continues listening, so the existing reservation is enlarged (reserveAdditionalAmount).  Suddenly, one of the teams scores a goal, so the match abruptly ends, leaving part of the reserved amount unused.  The provider now releases the reservation (releaseReservation), and the remaining amount is available for future use by the subscriber.

Now we can extend the second scenario by having the subscriber participate in a game of chance in which the provider refunds a percentage of the usage costs (refundAmount) based on the ranking of a particular team in this tournament.  For example, the subscriber gambling on the team that wins the tournament receives a full refund, while for gambling on the team that finishes in second place, the refund is 50%, etc.

## Amount Charging API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations are:

chargeAmount

refundAmount

Charge Currency Amount to an Account

chargeAmount(EndUserIdentifier endUserIdentifier, Decimal amount, String billingText, String referenceCode)

Behavior:

This message results in directly charging to the account indicated by the end user identifier.  The charge is specified as a currency amount.  The billing text field is used for textual information to appear on the bill. The reference code is used to uniquely identify the request; it is the application’s responsibility to provide a unique reference code within the scope of the application.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | The end user’s account to be charged |
| amount | Decimal | The currency amount of the charge |
| billingText | String | Textual information to appear on the bill |
| referenceCode | String | Textual information to uniquely identify the request, e.g. in case of disputes |

Exceptions:

UnknownEndUserException

InvalidArgumentException

ChargeFailureException

Refund Currency Amount to an Account

refundAmount(EndUserIdentifier endUserIdentifier, Decimal amount, String billingText, String referenceCode)

Behavior:

This message results in directly applying a refund to the account indicated by the end user identifier.  The refund is specified as a currency amount.  The billing text field is used for textual information to appear on the bill. The reference code is used to uniquely identify the request; it is the application’s responsibility to provide a unique reference code within the scope of the application.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | The end user’s account to be refunded |
| amount | Decimal | The currency amount of the refund |
| billingText | String | Textual information to appear on the bill |
| referenceCode | String | Textual information to uniquely identify the request, e.g. in case of disputes |

Exceptions:

UnknownEndUserException

InvalidArgumentException

ChargeFailureException

## Volume Charging API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations are:

chargeVolume

getAmount

refundVolume

Charge Volume to an Account

chargeVolume(EndUserIdentifier endUserIdentifier, Long volume, String billingText, String referenceCode)

Behavior:

This message results in directly charging to the account indicated by the end user identifier.  The charge is specified as a volume.  The billing text field is used for textual information to appear on the bill. The reference code is used to uniquely identify the request; it is the application’s responsibility to provide a unique reference code within the scope of the application.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | The end user’s account to be charged |
| volume | Long | The volume to be charged |
| billingText | String | Textual information to appear on the bill |
| referenceCode | String | Textual information to uniquely identify the request, e.g. in case of disputes |

Exceptions:

UnknownEndUserException

InvalidArgumentException

ChargeFailureException

Convert a Volume to a Currency Amount

getAmount(EndUserIdentifier endUserIdentifier, Long volume, out Decimal amount)

Behavior:

This message results in converting the given volume to a currency amount. The end user identifier is given to indicate the subscriber for whom this conversion calculation must be made.  The message returns a currency amount if successful.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | The end user’s account to be charged |
| volume | Long | The volume to be converted |
| amount | Decimal | OUTPUT. It is the currency amount resulting from the conversion process |

Exceptions:

UnknownEndUserException

InvalidArgumentException

ServiceException

Refund Volume to an Account

refundVolume(EndUserIdentifier endUserIdentifier, Long volume, String billingText, String referenceCode)

Behavior:

This message results in directly applying a refund to the account indicated by the end user identifier.  The refund is specified as a volume.  The billing text field is used for textual information to appear on the bill. The reference code is used to uniquely identify the request; it is the application’s responsibility to provide a unique reference code within the scope of the application.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | The end user’s account to be refunded |
| volume | Long | The volume to be refunded |
| billingText | String | Textual information to appear on the bill |
| referenceCode | String | Textual information to uniquely identify the request, e.g. in case of disputes |

Exceptions:

UnknownEndUserException

InvalidArgumentException

ChargeFailureException

## Reserved Amount Charging API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations are:

reserveAmount

reserveAdditionalAmount

chargeReservation

releaseReservation

Reserve a Currency Amount from an Account

reserveAmount(EndUserIdentifier endUserIdentifier, Decimal amount, String billingText, out String reservationIdentifier)

Behavior:

This message results in directly reserving an amount for an account indicated by the end user identifier.  The reservation is specified as a currency amount.  Note that reservations do not last forever; it is assumed the default reservation enforcement time is negotiated off-line. If the reservation times out, the remaining funds will be returned to the account from which this reservation was made. However, the remaining funds shall preferably be returned explicitly to the account using the releaseReservation message. The billing text field is used for textual information to appear on the bill.  Subsequent textual information provided during this charging session will be appended to this textual information; one charging session to a reservation will result in only one entry on the bill.  In case of success, a reservation id is returned for future reference; e.g. subsequent charging against the existing reservation using the chargeReservation message.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | The end user’s account subject to the reservation |
| amount | Decimal | The currency amount of the reservation |
| billingText | String | Textual information to appear on the bill |
| reservationIdentifier | String | OUTPUT. It is an identifier for the newly created reservation |

Exceptions:

UnknownEndUserException

InvalidArgumentException

ServiceException

Adjust the Currency Amount of an Existing Reservation

reserveAdditionalAmount(String reservationIdentifier, Decimal amount, String billingText)

Behavior:

This message results in the addition/reduction of a currency amount to/from an existing reservation indicated by the reservation id.  The reservation is specified as a currency amount.  Note that reservations do not last forever; it is assumed the default reservation enforcement time is negotiated off-line.  Invoking this message will extend the reservation enforcement time for another off-line-negotiated period. The billing text field is used for appending textual information to appear on the bill.  The textual information is appended to the initial textual information given by the reserveAmount message; one charging session to a reservation will result in only one entry on the bill.  Reserved credit can be returned to the account through the releaseReservation message.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| reservationIdentifier | String | An identifier for the reservation to be amended |
| amount | Decimal | The currency amount to be added to (or subtracted from) the reservation |
| billingText | String | Textual information to appear on the bill |

Exceptions:

UnknownReservationException

InvalidArgumentException

ServiceException

Charge a Currency Amount against an Existing Reservation

chargeReservation(String reservationIdentifier, Decimal amount, String billingText, String referenceCode)

Behavior:

This message results in charging to a reservation indicated by the reservation id.  Reservations, identified by reservation id, are established through invoking the reserveAmount message.  The charge is specified as a currency amount.  Optionally, the billing text field can be used for appending textual information to appear on the bill.  The textual information is appended to the initial textual information given by the reserveAmount message; one charging session to a reservation will result in only one entry on the bill. The reference code is used to uniquely identify the request; it is the application’s responsibility to provide a unique reference code within the scope of the application.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| reservationIdentifier | String | An identifier for the reservation to be charged |
| amount | Decimal | The currency amount of the charge |
| billingText | String | OPTIONAL. Textual information to appear on the bill |
| referenceCode | String | Textual information to uniquely identify the request, e.g. in case of disputes |

Exceptions:

UnknownReservationException

InvalidArgumentException

ChargeFailureException

Release an Existing Reservation

releaseReservation(String reservationIdentifier)

Behavior:

Returns funds left in a reservation indicated by reservation id to the account from which this reservation was made.  Reservations, identified by reservation id, are established by invoking the reserveAmount message.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| reservationIdentifier | String | An identifier for the reservation to be released |

Exceptions:

UnknownReservationException

ServiceException

## Reserved Volume Charging API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations are:

getAmount

reserveVolume

reserveAdditionalVolume

chargeReservation

releaseReservation

Convert a Volume to a Currency Amount

getAmount(EndUserIdentifier endUserIdentifier, Long volume, out Decimal amount)

Behavior:

Returns the amount resulting from converting the given volume.  The end user identifier is given to indicate the subscriber for whom this calculation must be made.  The message returns a currency amount if successful.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | The end user’s account to be charged |
| volume | Long | The volume to be converted |
| amount | Decimal | OUTPUT. It is the currency amount resulting from the conversion process |

Exceptions:

UnknownEndUserException

InvalidArgumentException

ServiceException

Reserve a Volume from an Account

reserveVolume(EndUserIdentifier endUserIdentifier, Long volume, String billingText, out String reservationIdentifier)

Behavior:

Reserves an amount of an account indicated by the end user identifier.  The reservation is specified as a volume.  Note that reservations do not last forever; it is assumed the default reservation enforcement time is negotiated off-line. If the reservation times out, the remaining volume will be returned to the account from which this reservation was made. However, the remaining volume should preferably be returned explicitly to the account using the releaseReservation message.  The billing text field is used for textual information to appear on the bill.  Subsequent textual information provided during this charging session will be appended to this textual information; one charging session to a reservation will result in only one entry on the bill.  In case of success, a reservation identifier is returned for future reference; e.g. subsequent charging against the existing reservation using the chargeReservation message.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | The end user’s account subject to the reservation |
| volume | Long | The volume of the reservation |
| billingText | String | Textual information to appear on the bill |
| reservationIdentifier | String | OUTPUT. It is an identifier for the newly created reservation |

Exceptions:

UnknownEndUserException

InvalidArgumentException

ServiceException

Adjust the Volume of an Existing Reservation

reserveAdditionalVolume(String reservationIdentifier, Long volume, String billingText)

Behavior:

Adds/reduces a volume to an existing reservation indicated by the reservation id.  The reservation is specified as a volume.  Note that reservations do not last forever; it is assumed the default reservation enforcement time is negotiated off-line.  Invoking this message will extend the reservation enforcement time for another off-line-negotiated period.  The billing text field is used for appending textual information to appear on the bill.  The textual information is appended to the initial textual information given by the reserveVolume message; one charging session to a reservation will result in only one entry on the bill.  A reserved credit can be returned to the account through the releaseReservation message.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| reservationIdentifier | String | An identifier for the reservation to be amended |
| volume | Long | The volume to be added to (or subtracted from) the reservation |
| billingText | String | Textual information to appear on the bill |

Exceptions:

UnknownReservationException

InvalidArgumentException

ServiceException

Charge a Volume against an Existing Reservation

chargeReservation(String reservationIdentifier, Long volume, String billingText, String referenceCode)

Behavior:

This message results in charging to a reservation indicated by the reservation id..  Reservations, identified by reservation id., are established through invoking the reserveVolume message.  The charge is specified as a volume. Optionally, the billing text field can be used for appending textual information to appear on the bill.  The textual information is appended to the initial textual information given by the reserveVolume message; one charging session to a reservation will result in only one entry on the bill. The reference code is used to uniquely identify the request; it is the application’s responsibility to provide a unique reference code within the scope of the application.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| reservationIdentifier | String | An identifier for the reservation to be charged |
| volume | Long | The currency amount of the charge |
| billingText | String | OPTIONAL. Textual information to appear on the bill |
| referenceCode | String | Textual information to uniquely identify the request, e.g. in case of disputes |

Exceptions:

UnknownReservationException

InvalidArgumentException

ChargeFailureException

Release an Existing Reservation

releaseReservation(String reservationIdentifier)

Behavior:

Returns funds left in a reservation indicated by reservation id. to the account from which this reservation was made.  Reservations, identified by reservation id., are established through invoking the reserveVolume message.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| reservationIdentifier | String | An identifier for the reservation to be released |

Exceptions:

UnknownReservationException

ServiceException

## Web Service Data Definitions

Data Types

All data types are defined in Section 2.2.

Exceptions

In addition to the Common Exceptions defined in Section 2.3, there are exceptions specific to this Web Service.  Similar to the Common Exceptions, each Web Service-specific exception is assigned an eight character identifier. This identifier is interpreted as described in Section 2.3, except that the first 3 characters uniquely identify this Web Service.

The following exceptions are specific to this Web Service:

| UNIQUE ID | TEXT STRING | MEANING |
| --- | --- | --- |
| PAY1000E | ChargeFailureException | Indicates that an error occurred when attempting to charge to the account. The charge did not occur. |
| PAY1001F | UnknownReservation Exception | Indicates that the passed reservation identifier is unknown. |
| PAY1002E | UnknownReservation Exception | Indicates that the passed reservation identifier is unavailable; it may have timed out according to the policy in place. |

## Web Service Syntax – WSDL

The rpc/literal files are

- parlayx_payment_service_port.wsdl

- parlayx_payment_amount_charging_service

- parlayx_payment_volume_charging_service

- parlayx_payment_reserve_amount_charging_service

- parlayx_payment_reserve_volume_charging_service

The rpc/encoded file is

- parlayx_payment_service.wsdl

# Account Management

## Record of Changes

This sub-section will be used in the future for tracking changes to version 1.0 (and any later versions) of the Payment Web Service.  It will consist of four parts capturing changes to Messages, Data Definitions, Exceptions and ‘Others’, as appropriate.

## Overview

Description

Pre-paid subscribers, whether they have subscribed to pre-paid telephony, SMS, or data service, have credits with their service providers; the consumption of services will lead to reduction of their credit, or the credit may expire.  Therefore, from time to time, subscribers may have to recharge their accounts.  This occurs through an application that interfaces with the subscriber either directly or indirectly.  Examples of direct interaction are voice prompts and WAP/web pages, or even SMS.  Typically, such multi-modal applications either request a currency amount and, e.g. credit card information, or a voucher number plus credentials.  The voucher number and credentials are then validated and causes a pre-determined currency amount to be transferred.

The Parlay X Account Management API described in this document supports account querying, direct recharging and recharging through vouchers.  As a side effect, it may prevent subscribers from having their account balance credits expire.

Commercial & Technical Rationale

The recharging process is a critical component of telecom networks. At present, a number of prepaid services exist: e.g. Voice, SMS, and GPRS.  The Account Management Web Service:

- further enlarges the market for third party software and outsourcing as it supports subscriber self service through re-charging, account querying and prevents subscriber credits from expiring

- enables subscriber “self-service” through trusted and authenticated service or content providers

- allows recharging by subscriber address (e.g. MSISDN and PIN).

Relationship to Similar or Supplanted Specifications

Parlay/OSA have developed powerful, carrier-grade Content-Based Charging (CBC) and Account Management (AM) APIs.  The CBC APIs can be used to do recharging, but they also enable many other functions (e.g. debiting from accounts) as well.  The AM APIs support some subscriber self-service (i.e. query functions), but they are not as comprehensive as the Account Management Web Service.

Scenarios

This section discusses three scenarios; one where a subscriber uses a voucher, one where the subscriber directly recharges after the payment is cleared, and one where the subscriber checks the recent transactions. Note, associated Account Management API messages are shown in ‘bold’ format: e.g. (getBalance).

Scenario #1:

The prepaid subscriber wishes to recharge their account with a voucher and query their account balance.  The subscriber uses their mobile phone or other wireline phone to interact with an IVR system.  In order to recharge their account, the subscriber must enter the voucher number, the MSISDN to be recharged , and PIN(s).  The IVR system accesses an external voucher database to validate the voucher number. The subscriber's account balance is then increased with the value of the voucher (voucherUpdate).  The subscriber queries their account balance (getBalance), before and/or after the recharge.

Scenario #2:

Directly recharging (i.e. without a voucher) works much along the same way.  In this case, we assume the prepaid subscriber interacts with a web page.  After providing the MSISDN, along with the PIN, the user can query the account balance (getBalance).  For recharging, the subscriber must enter payment details, for example credit card information, from which the payment will be made.  After clearing the payment details, the currency amount will be transferred and the subscriber's prepaid account balance expiration date will be reset (balanceUpdate).   The subscriber also queries their account balance expiration date (getCreditExpiryDate), after the recharge.

Scenario #3:

Every time a subscriber makes a telephone call the balance of their prepaid account is decremented with the cost of the call.  When a recharge is done, the balance is increased either directly (balanceUpdate) or with an amount represented by a voucher (voucherUpdate).  When a subscriber has doubts about the correctness of the account balance, the subscriber can request the last transactions on the account and verify them (getHistory).  By offering automated access to this information, a call to the Operator's Help Desk is prevented which saves operational costs.

## Account Management API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations are:

getBalance

getCreditExpiryDate

balanceUpdate

voucherUpdate

getHistory

Note that certain parameters are negotiated off line.  For example the reseller identifier, which identifies the reseller of calling cards.

Account Balance Query

getBalance(EndUserIdentifier endUserIdentifier, String endUserPin, out Decimal amount)

Behavior:

This message results in getting account balance indicated by the end user identifier and associated end user PIN.  The returned amount is specified as a currency amount.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | This parameter identifies the end user's account. |
| endUserPin | String | Contains the end user's credentials for authorizing access to the account |
| amount | Decimal | OUTPUT. It is the balance on the end user's account. |

Exceptions:

InvalidArgumentException

ServiceException

PolicyException

EndUserAuthenticationException

Account Credit Expiration Date Query

getCreditExpiryDate(EndUserIdentifier endUserIdentifier, String endUserPin, out DateTime date)

Behavior:

This message results in getting the expiration date of the credit indicated by the end user identifier and associated end user PIN.  The returned date is the date the current balance will expire.  Nil is returned if the balance does not expire.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | This parameter identifies the end user's account. |
| endUserPin | String | Contains the end user's credentials for authorizing access to the account. |
| date | DateTime | OUTPUT. It is the date the current balance will expire. Nil is returned if the balance does not expire. |

Exceptions:

InvalidArgumentException

ServiceException

PolicyException

EndUserAuthenticationException

Account Balance Recharging

balanceUpdate(EndUserIdentifier endUserIdentifier, String endUserPin, String referenceCode, Decimal amount, Integer period)

Behavior:

This message results in directly recharging the account indicated by the end user identifier and optional associated end user PIN. The reference code is used to uniquely identify the request; it is the application’s responsibility to provide a unique reference code within the scope of the application.  The charge is specified as a currency amount.  The balance is requested to expire in the number of days indicated by the period parameter.  The operator’s policies may overrule this parameter.  If the optional period parameter is not present, the operator's policy on balance expiration is always in effect.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | This parameter identifies the end user's account. |
| endUserPin | String | OPTIONAL. Contains the end user's credentials for authorizing access to the account. |
| referenceCode | String | Textual information to uniquely identify the request, e.g. in case of disputes |
| amount | Decimal | Currency amount that should be added to the end user's account. |
| period | Integer | OPTIONAL. The balance is requested to expire in the number of days indicated by this parameter. The operator’s policies may overrule this parameter. If this optional parameter is not present, the operator's policy on balance expiration is always in effect. |

Exceptions:

InvalidArgumentException

ServiceException

PolicyException

EndUserAuthenticationException

Account Balance Voucher Recharging

voucherUpdate(EndUserIdentifier endUserIdentifier, String endUserPin, String referenceCode, String voucherIdentifier, String voucherPin)

Behavior:

This message results in directly recharging the account indicated by the end user identifier and optional associated end user PIN. The reference code is used to uniquely identify the request; it is the application’s responsibility to provide a unique reference code within the scope of the application.  A voucher identifier indirectly specifies the charge.  The optional voucher PIN code can be used to verify the voucher.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | This parameter identifies the end user's account. |
| endUserPin | String | OPTIONAL. Contains the end user's credentials for authorizing access to the account. |
| referenceCode | String | Textual information to uniquely identify the request, e.g. in case of disputes |
| voucherIdentifier | String | This parameter identifies the voucher. |
| voucherPin | String | OPTIONAL. Contains the voucher's credentials for authentication. |

Exceptions:

InvalidArgumentException

UnknownVoucherException

ServiceException

PolicyException

EndUserAuthenticationException

Account Transaction History Query

getHistory(EndUserIdentifier endUserIdentifier, String endUserPin, DateTime date, Integer maxEntries, out DatedTransaction[] history)

Behavior:

This message results in returning the transaction history of the account indicated by the end user identifier and associated optional end user PIN.  The maximum number of entries to return and the start date define the range of transactions that are of interest to the requester.

If the total number of entries in the transaction history, starting at the specified date, is larger than the specified maximum number of entries, only the most recent events are returned.  Note that the operator might limit the maximum amount of entries to be returned or the period for which the entries are to be returned.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUserIdentifier | EndUserIdentifier | This parameter identifies the end user's account. |
| endUserPin | String | OPTIONAL. Contains the end user's credentials for authorizing access to the account. |
| date | DateTime | OPTIONAL. This parameter indicates the desired starting date for the entries to be returned. If this parameter is not present, it is up to the discretion of the service to decide this date. |
| maxEntries | Integer | OPTIONAL. This parameter indicates the maximum number of entries that shall be returned. If this parameter is not present, it is up to the discretion of the service to decide how many entries to return. |
| history | Array of DatedTransaction | OUTPUT. It is a DatedTransaction array that consists of types with a date field and a string field: i.e. the date of the occurrence and the transaction details, respectively. |

Exceptions:

InvalidArgumentException

ServiceException

PolicyException

EndUserAuthenticationException

## Web Service Data Definitions

Data Types

In addition to the Common Data Types defined in Section 2.2, the following Data Types are specific to this Web Service.

DatedTransaction

The DatedTransaction data type is a structure containing the following parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| transactionDate | DateTime | The date the transaction occurred. |
| transactionDetails | String | The transaction details. |

Exceptions

In addition to the Common Exceptions defined in Section 2.3, there are exceptions specific to this Web Service.  Similar to the Common Exceptions, each Web Service-specific exception is assigned an eight character identifier. This identifier is interpreted as described in Section 2.3, except that the first 3 characters uniquely identify this Web Service.

The following exceptions are specific to this Web Service:

| UNIQUE ID | TEXT STRING | MEANING |
| --- | --- | --- |
| ACM1000E | UnknownVoucherException | This fault occurs if the voucher identification that is passed is unknown. |
| ACM1001E | EndUserAuthentication Exception | This fault occurs if either the end user identification that is passed is unknown, the end user's credentials are required but are not passed, or the end user’s credentials are passed but are invalid. |

## Web Service Syntax – WSDL

The rpc/literal files are

- parlayx_account_management_types.xsd

- parlayx_account_management_service_port.wsdl

- parlayx_account_management_service.wsdl

The rpc/encoded file is

- parlayx_account_management_service.wsdl

# User Status

## Record of Changes

This sub-section will be used in the future for tracking changes to version 1.0 (and any later versions) of the User Status Web Service.  It will consist of four parts capturing changes to Messages, Data Definitions, Exceptions and ‘Others’, as appropriate.

## Overview

Description

The Parlay X User Status Web Service will be used for getting user status information. The use of the Web Service will not require any specific telecommunication skills.

Commercial & Technical Rationale

The use of a Parlay X User Status Web Service will enable fast and easy development of user status aware applications.

Relationship to Similar or Supplanted Specifications

The Parlay/OSA Mobility (User Status) Service API can also provide user status information, but the Parlay X API for this Web Service is easier to use.

The Parlay/OSA Presence and Availability Management Service specifies a set of interfaces for applications that provide broader presence and availability capabilities than those currently defined for this Web Service. These capabilities will be considered for inclusion in future Parlay X Web Services.

Scenarios

In the following, two sample Scenarios are described.

Buddy-list

This application is a mobile version of services like ICQ, MSN Messenger Service and Yahoo! Messenger, which offer text and voice chat and text conferencing. With a mobile terminal the user can be always on.

The user of the service can define one or more buddy-lists containing their friends (alternatively their family, colleagues or a combination). The status of buddies can be shown in the Buddy-list

Manual call routing

When a switchboard receives a call, the switchboard operator may obtain the status of a mobile terminal before trying to route the call to it.

## User Status API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations are:

getUserStatus

Get User Status

getUserStatus(EndUserIdentifier endUser, EndUserIdentifier requester, out UserStatusData userStatus)

Behavior:

Requests the user status information of a user.  Before returning the user status indicator, end-user and operator policies must be satisfied.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUser | EndUserIdentifier | It identifies the end user for whom user status information is being requested. |
| requester | EndUserIdentifier | OPTIONAL. The address of the requester. |
| userStatus | UserStatusData | OUTPUT. It is the user status of the end user |

Exceptions:

InvalidArgumentException

UnknownEndUserException

ServiceException

PolicyException

## Web Service Data Definitions

Data Types

In addition to the Common Data Types defined in Section 2.2, the following Data Types are specific to this Web Service.

UserStatusData

The UserStatusData data type is a structure containing the following parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| userStatusIndicator | UserStatusIndicator | It indicates the status of the end user. |
| additionalUserStatus Information | String | A string to hold additional information if the userStatusIndicator is ‘Other’. |

UserStatusIndicator

The UserStatusIndicator data type is an enumeration with the following values:

| VALUE | DESCRIPTION |
| --- | --- |
| Online | User is online. |
| Offline | User is offline (mobile terminal switched off/other terminal not connected to the service), or wants to appear to be offline. |
| Busy | User is busy. |
| Other | Custom user status information can be retrieved from additionalUserStatusInformation. |

Exceptions

All exceptions thrown by this Web Service are Common Exceptions, as defined in Section 2.3.

## Web Service Syntax – WSDL

The rpc/literal files are

- parlayx_user_status_types.xsd

- parlayx_user_status_service_port.wsdl

- parlayx_user_status_service.wsdl

The rpc/encoded file is

- parlayx_user_status_service.wsdl

# Terminal Location

## Record of Changes

This sub-section will be used in the future for tracking changes to version 1.0 (and any later versions) of the Terminal Location Web Service.  It will consist of four parts capturing changes to Messages, Data Definitions, Exceptions and ‘Others’, as appropriate.

## Overview

Description

The Parlay X Terminal Location Web Service will be used for getting location information. The use of the Web Service will not require any specific telecommunication skills, but knowledge of location co-ordinates will be required.

Commercial & Technical Rationale

The use of a Parlay X Terminal Location Web Service will enable fast and easy development of location aware Applications. The use of the Web Service will only require knowledge of longitude and latitude from the World Geodetic System 1984 (WGS 84), which is the reference system chosen for the coding of locations.

The market for location aware services is growing, and easy access to location information will stimulate the growth of this market.

Relationship to Similar or Supplanted Specifications

The Ericsson Mobile Positioning System (MPS) offers much of the same functionality that the Parlay X Terminal Location Web Service will offer.

Scenarios

In the following, a sample Scenario is described.

### Location enabled Buddy-list:

This application is a mobile version of services like ICQ, MSN Messenger Service and Yahoo! Messenger, which offer text and voice chat and text conferencing. With a mobile terminal the user can be always on, and the service can also show where buddies are located.

The user of the service can define one or more buddy-lists containing their friends (alternatively their family, colleagues or a combination). The Buddy List application may access terminal location information, and the following two cases are considered: a user initiates the retrieval of i) its own location and ii) other users’ location.

## Terminal Location API

This section describes an initial set of capabilities in terms of message invocations, parameters and data types.  The message-based invocations are:

getLocation

Get Location of Terminal

getLocation(EndUserIdentifier endUser, EndUserIdentifier requester, LocationAccuracy accuracy, out LocationInfo location)

Behavior:

Requests the location of one terminal. The location is returned if the terminal is available. Before returning the location, end-user and operator policies must be satisfied.

Parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| endUser | EndUserIdentifier | The address of the terminal for which location information is being requested. |
| requester | EndUserIdentifier | OPTIONAL. The address of the terminal from which the request is initiated. |
| accuracy | LocationAccuracy | The desired accuracy. Possible values are: ‘Low’, ‘Medium’, ‘High’. Each operator must assign a “radius of uncertainty” to each value (e.g. < 3km, < 1km, < 100m, respectively) |
| location | LocationInfo | OUTPUT. It identifies the location of the terminal. |

Exceptions:

InvalidArgumentException

UnknownEndUserException

ServiceException

PolicyException

## Web Service Data Definitions

Data Types

In addition to the Common Data Types defined in Section 2.2, the following Data Types are specific to this Web Service.

LocationInfo

The LocationInfo data type is a structure containing the following parameters:

| NAME | TYPE | DESCRIPTION |
| --- | --- | --- |
| longitude | Float | Longitude |
| latitude | Float | Latitude |
| accuracy | LocationAccuracy | How accurate the Location information is. If the degree of accuracy wanted is available this should be given, if not the best possible accuracy should be returned. Possible values are: ‘Low’, ‘Medium’, ‘High’. |
| dateTime | DateTime | Identifies when the location information was obtained. |

LocationAccuracy

The LocationAccuracy data type is an enumeration with the following values: (Each Parlay X  Gateway operator must specify the uncertainty radiuses for Low, Medium and High)

| VALUE | DESCRIPTION |
| --- | --- |
| Low | Low accuracy i.e. < 3km radius of uncertainty. |
| Medium | Medium accuracy i.e. < 1km radius of uncertainty. |
| High | High accuracy i.e. < 100m radius of uncertainty. |

Exceptions

All exceptions thrown by this Web Service are Common Exceptions, as defined in Section 2.3.

## Web Service Syntax – WSDL

The rpc/literal files are

- parlayx_terminal_location_types.xsd

- parlayx_terminal_location_service_port.wsdl

- parlayx_terminal_location_service.wsdl

The rpc/encoded file is

- parlayx_terminal_location_service.wsdl

Index of Parlay X API Messages

The following is an alphabetical index of message names defined in the Parlay X Web Service sections of this document, i.e. from section 3 onwards.

- Message names in italics represent invocations of an application web service by a Parlay X Web Service implementation (running on a Parlay X Gateway).

INDEX

balanceUpdate(EndUserIdentifier endUserIdentifier, String endUserPin, String referenceCode, Decimal amount, Integer period)	78

cancelCallRequest (String callIdentifier)	24

chargeAmount(EndUserIdentifier endUserIdentifier, Decimal amount, String billingText, String referenceCode)	63

chargeReservation(String reservationIdentifier, Decimal amount, String billingText, String referenceCode)	68

chargeReservation(String reservationIdentifier, Long volume, String billingText, String referenceCode)	72

chargeVolume(EndUserIdentifier endUserIdentifier, Long volume, String billingText, String referenceCode)	64

endCall(String callIdentifier)	23

getAmount(EndUserIdentifier endUserIdentifier, Long volume, out Decimal amount)	70

getAmount(EndUserIdentifier endUserIdentifier, Long volume, out Decimal amount)	65

getBalance(EndUserIdentifier endUserIdentifier, String endUserPin, out Decimal amount)	77

getCallInformation(String callIdentifier, out CallInformationType callInformation)	23

getCreditExpiryDate(EndUserIdentifier endUserIdentifier, String endUserPin, out DateTime date)	77

getHistory(EndUserIdentifier endUserIdentifier, String endUserPin, DateTime date, Integer maxEntries, out DatedTransaction[] history)	80

getLocation(EndUserIdentifier endUser, EndUserIdentifier requester, LocationAccuracy accuracy, out LocationInfo location)	87

getMessage(String messageRefIdentifier)   Attachments[out content]	55

getMessageDeliveryStatus(String requestIdentifier, out DeliveryStatusType[] deliveryStatus)	52

getMessageURLs(String messageRefIdentifier, out MessageURL message)	54

getReceivedMessages(String registrationIdentifier, MessagePriority priority, out MessageRef [] messageRef)	53

getReceivedSms(String registrationIdentifier, out SmsType[] receivedSms)	45

getSmsDeliveryStatus(String requestIdentifier, out DeliveryStatusType[] deliveryStatus)	43

getUserStatus(EndUserIdentifier endUser, EndUserIdentifier requester, out UserStatusData userStatus)	84

handleBusy(EndUserIdentifier callingParty, EndUserIdentifier callingParty, out Action action)	29

handleCalledNumber(EndUserIdentifier callingParty, EndUserIdentifier calledParty, out Action action)	32

handleNoAnswer(EndUserIdentifier callingParty, EndUserIdentifier calledParty, out Action action)	31

handleNotReachable(EndUserIdentifier callingParty, EndUserIdentifier calledParty, out Action action)	30

handleOffHook(EndUserIdentifier callingParty, out Action action)	33

makeACall(EndUserIdentifier callingParty, EndUserIdentifier calledParty, String charging, out String callIdentifier)	22

notifyMessageReception (String registrationIdentifier, MessageRef messageRef)	56

notifySmsReception(String registrationIdentifier, String smsServiceActivationNumber, EndUserIdentifier senderAddress, String message)	44

refundAmount(EndUserIdentifier endUserIdentifier, Decimal amount, String billingText, String referenceCode)	63

refundVolume(EndUserIdentifier endUserIdentifier, Long volume, String billingText, String referenceCode)	66

releaseReservation(String reservationIdentifier)	69, 73

reserveAdditionalAmount(String reservationIdentifier, Decimal amount, String billingText)	68

reserveAdditionalVolume(String reservationIdentifier, Long volume, String billingText)	71

reserveAmount(EndUserIdentifier endUserIdentifier, Decimal amount, String billingText, out String reservationIdentifier)	67

reserveVolume(EndUserIdentifier endUserIdentifier, Long volume, String billingText, out String reservationIdentifier)	71

sendMessage(EndUserIdentifier [] destinationAddressSet, String senderAddress, String subject, MessagePriority priority, String charging, out String requestIdentifier)  Attachment[content]	50

sendSms(EndUserIdentifier[] destinationAddressSet, String senderName, String charging, String message, out String requestIdentifier)	39

sendSmsLogo(EndUserIdentifier[] destinationAddressSet, String senderName, String charging, Base64Binary image, SmsFormat smsFormat, out String requestIdentifier)	40

sendSmsRingtone(EndUserIdentifier[] destinationAddressSet, String senderName, String charging, String ringtone, SmsFormat smsFormat, out String requestIdentifier)	41

voucherUpdate(EndUserIdentifier endUserIdentifier, String endUserPin, String referenceCode, String voucherIdentifier, String voucherPin)	79

# Footnotes

EMS (Enhanced Messaging Service) is an enhancement to SMS that provides the ability to send a combination of simple melodies, pictures, sounds, animations, modified text and standard text as an integrated message for display on an EMS compliant handset. EMS is standardized in 3GPP TS 23.040 where the coding mechanisms and formats are specified.

RTX Ringtone Specification : An RTX file is a text file, containing the ringtone name, a control section and a section containing a comma separated sequence of ring tone commands.

SOAP-Attachment is used because specification of the WS-Attachments standard is not yet complete. The decision to use SOAP-Attachment may be revisited in future releases.  Please refer to your SOAP/WSDL toolkit documentation for information on populating or retrieving a SOAP-Attachment.

SOAP-Attachment is used because specification of the WS-Attachments standard is not yet complete. The decision to use SOAP-Attachment may be revisited in future releases.  Please refer to your SOAP/WSDL toolkit documentation for information on populating or retrieving a SOAP-Attachment.